## Slide 1: Independent Load Forecast Stakeholder Workshop #2
April 18, 2016

## Slide 2: Stakeholder Feedback
Use of binary variables instead of after-the-fact adjustment for seasonal peaks
  We think this potentially has merit but was not incorporated last year due to time limitations. Preliminary investigations had some issues with variables being statistically insignificant, but we will look at this more thoroughly this year.

## Slide 3: Stakeholder Feedback
Use of end-use or SAE models to measure historical DSM
  Unfortunately, this would require access to data that we don’t have, such as load shape information at the state level

## Slide 4: Stakeholder Feedback
Develop separate Louisiana models with and without CHP and use our judgment
  Will discuss this in the section on the state econometric models

## Slide 5: Stakeholder Feedback
Use of state-level electricity price variable is inappropriate because price is a function of electricity consumption
  We disagree for a number of reasons, including that our models use either lagged prices or moving average prices and today’s consumption does not affect previous year’s prices

## Slide 6: Considerations When Comparing Past Forecasts to Actual
Actual weather conditions could be quite different than normal
Energy efficiency requirements may have changed
Forecasts may reflect demand response that was available but not used
The geographic footprint may have changed
It is unlikely that significant economic events were foreseen

## Slide 7: Forecast Comparison 2016-2025 2015 ILF to Module E for PY2016

## Slide 8: Module E Data
Module E forecasts provide a series of projections of non-coincident peaks at the asset owner level (24 months followed by 8 years of summer and winter peaks)
Zonal and system coincident peak values are provided for a single year
We calculated zonal and system coincidence factors from these values and applied them to the projected values (not available for winter) to find LRZ non-coincident and system coincident peaks

## Slide 9: Forecast Comparisons
ILF
Allocates state-level forecasts to LRZ levels;
Uses conversion factors to determine LRZ non-coincident peaks and coincidence factors to determine system-wide peak load;
Net load: with EE/DR/DG adjustment;
Gross load: without EE/DR/DG adjustment.
MISO Module E
Aggregates asset owner level loads to LRZ levels;
Applies intra-zonal/MISO-wide coincidence factors to convert asset owner level peak loads to zonal peaks and system-wide peak load;
Does not include DR/DG adjustment, may include EE adjustment.

## Slide 10: Comparison Charts
Module E – solid black line
ILF Gross – dashed black line
  ILF Gross high/low bands – hashed area
ILF Net – dashed red line
  ILF Net high/low bands – solid area
2014 actual value – diamond
  Note: 2014 was a mild summer, so weather normal peaks would likely be higher

## Slide 11: SUFG Gross & Net Forecast vs. Module E — LRZ 1

## Slide 12: SUFG Gross & Net Forecast vs. Module E — LRZ 2

## Slide 13: SUFG Gross & Net Forecast vs. Module E — LRZ 3

## Slide 14: SUFG Gross & Net Forecast vs. Module E — LRZ 4

## Slide 15: SUFG Gross & Net Forecast vs. Module E — LRZ 5

## Slide 16: SUFG Gross & Net Forecast vs. Module E — LRZ 6

## Slide 17: SUFG Gross & Net Forecast vs. Module E — LRZ 7

## Slide 18: SUFG Gross & Net Forecast vs. Module E — LRZ 8

## Slide 19: SUFG Gross & Net Forecast vs. Module E — LRZ 9

## Slide 20: SUFG Gross & Net Forecast vs. Module E — LRZ 10

## Slide 21: SUFG Gross & Net Forecast vs. Module E — MISO System

## Slide 22: Historical Summer Peak Demand* (Metered Load in MW)
LRZ | 2010 | 2011 | 2012 | 2013 | 2014
1 | 15,992 | 17,601 | 17,996 | 17,909 | 17,018
2 | 12,392 | 13,164 | 13,228 | 12,639 | 11,730
3 | 8,534 | 8,991 | 9,188 | 8,880 | 8,283
4 | 9,863 | 10,277 | 10,409 | 9,523 | 9,563
5 | 9,084 | 9,129 | 9,171 | 8,428 | 8,487
6 | 16,391 | 18,324 | 18,302 | 17,629 | 17,170
7 | 20,633 | 22,232 | 22,655 | 21,598 | 19,293
8 | 7,323 | 8,002 | 7,488 | 7,033 | 7,058
9 | 18,777 | 19,218 | 19,223 | 19,517 | 19,173
10 | 4,633 | 4,919 | 4,847 | 4,648 | 4,297
MISO | 118,833 | 127,556 | 126,590 | 122,445 | 114,709
* LRZ values are non-coincident with MISO system peak

## Slide 23: Annual Energy and Winter Peak Demands
We have not been provided annual energy numbers for comparison
The lack of information on winter peak coincidence at the zonal and system levels means that any comparison would bias the Module E results high
  We would be comparing the sum of asset owner non-coincident peaks to ILF forecasts that are either coincident within the LRZ or within the system

## Slide 24: State Econometric Models

## Slide 25: Model Development
We used a similar process to last year to find models with a good fit, with an appropriate mix of explanatory variables, and that passed the tests for serial correlation and heteroskedasticity.
Added another year of history (2014)
Used the population-weighted virtual weather stations that were developed last year
For some states, changes were made to the explanatory variables or sample periods
  changes (if any) are shown for each state

## Slide 26: Dependent and Explanatory Variables
Variables | Eviews name | Units
Dependent variable: |  | 
Electricity sales | ELECTRICITY_SALES | Gwhs
Explanatory variables: |  | 
Electricity prices | REAL_ELECTRICITY_PRICE | Cents/Kwh in 2009 dollars *
Natural gas prices | REAL_NATURAL_GAS_PRICE | Dollars/Mcf in 2009 dollars *
Real personal income | REAL_INCOME | Thousands of 2009 dollars
Population | POPULATION | Number of people
Manufacturing employment | MANUFACTURING_EMP | Number of jobs
Non-manufacturing employment | NON_MANUFACTURING_EMP | Number of jobs
Non-farm employment | NON_FARM_EMP | Number of jobs
Gross state product | REAL_GSP | Millions in 2009 dollars
Cooling degree days | CDD | Fahrenheit (base 65)
Heating degree days | HDD | Fahrenheit (base 65)
* Original data was in nominal dollars. SUFG converted it to real 2009 dollars using state level CPI from IHS Global Insight. |  | 

## Slide 27: Statistical Tests
Correlogram Q Statistics (Test for serial correlation)
Breusch-Godfrey LM Test (Test for serial correlation)
White Test (Test for heteroskedasticity)
Chow Breakpoint Test (Test for model stability)
Histogram Normality Test

## Slide 28: Arkansas
Change: electricity price uses 4-year moving averages instead of 3-year moving averages previously
Dependent Variable: ELECTRICITY_SALES |  |  |  |  | 
Method: Least Squares |  |  |  |  | 
Sample: 1990 2014 |  |  |  |  | 
Included observations: 25 |  |  |  |  | 
Variable | Coefficient | Std. Error | t-Statistic | Prob. | Elasticity at 2014 (weather at means)
C | 18922.77 | 3202.394 | 5.908946 | 0.0000 | 
@MOVAV(REAL_ELECTRICITY_PRICE,4) | -1644.084 | 176.6988 | -9.304444 | 0.0000 | -0.2484
GSP | 0.278528 | 0.016122 | 17.27614 | 0.0000 | 0.6491
CDD | 3.56418 | 0.488213 | 7.300467 | 0.0000 | 0.1590
HDD | 1.082386 | 0.358589 | 3.018457 | 0.0068 | 0.0928
R-squared | 0.994928 | Mean dependent var |  | 40551.61 | 
Adjusted R-squared | 0.993914 | S.D. dependent var |  | 6716.979 | 
S.E. of regression | 524.0147 | Durbin-Watson stat |  | 1.575739 | 
F-statistic | 980.8533 |  |  |  | 
Prob(F-statistic) | 0.000000 |  |  |  | 

## Slide 29: Illinois
Dependent Variable: ELECTRICITY_SALES |  |  |  |  | 
Method: Least Squares |  |  |  |  | 
Sample: 1990 2014 |  |  |  |  | 
Included observations: 25 |  |  |  |  | 
Variable | Coefficient | Std. Error | t-Statistic | Prob. | Elasticity at 2014 (weather at means)
C | 88116.68 | 14962.59 | 5.889134 | 0.0000 | 
@MOVAV(REAL_ELECTRICITY_PRICE,5) | -2367.163 | 612.858 | -3.862499 | 0.0010 | -0.1419
GSP | 0.082279 | 0.014402 | 5.712963 | 0.0000 | 0.3891
CDD | 10.70239 | 1.338207 | 7.997555 | 0.0000 | 0.0778
HDD | 1.510145 | 0.570358 | 2.647716 | 0.0154 | 0.0670
R-squared | 0.99072 | Mean dependent var |  | 133512.2 | 
Adjusted R-squared | 0.988864 | S.D. dependent var |  | 10743.76 | 
S.E. of regression | 1133.768 | Durbin-Watson stat |  | 1.978099 | 
F-statistic | 533.7845 |  |  |  | 
Prob(F-statistic) | 0.000000 |  |  |  | 
No changes in drivers or starting year from 2015 model

## Slide 30: Indiana
Change: natural gas price uses 2-year moving averages instead of 3-year moving averages previously
Dependent Variable: ELECTRICITY_SALES |  |  |  |  | 
Method: Least Squares |  |  |  |  | 
Sample: 1990 2014 |  |  |  |  | 
Included observations: 25 |  |  |  |  | 
Variable | Coefficient | Std. Error | t-Statistic | Prob. | Elasticity at 2014 (weather at means)
C | 23938.99 | 3441.989 | 6.954987 | 0.0000 | 
@MOVAV(REAL_ELECTRICITY_PRICE,3) | -1225.3 | 227.6832 | -5.381601 | 0.0000 | -0.0944
@MOVAV(REAL_NATURAL_GAS_PRICE,2) | 363.4235 | 103.8457 | 3.499648 | 0.0024 | 0.0246
REAL_GSP | 0.252658 | 0.004863 | 51.95145 | 0.0000 | 0.6810
CDD | 6.156419 | 0.764461 | 8.053285 | 0.0000 | 0.0674
HDD | 1.813066 | 0.381139 | 4.756967 | 0.0001 | 0.1033
R-squared | 0.996911 | Mean dependent var |  | 96216.86 | 
Adjusted R-squared | 0.996098 | S.D. dependent var |  | 10913.56 | 
S.E. of regression | 681.7222 | Durbin-Watson stat |  | 2.007218 | 
F-statistic | 1226.353 |  |  |  | 
Prob(F-statistic) | 0.000000 |  |  |  | 

## Slide 31: Iowa
Changes: starting year has been changed from 1990 to 1993; electricity price has been replaced by a 2-year lagged electricity price; per capita income and real GSP have been replaced by total income
Dependent Variable: ELECTRICITY_SALES |  |  |  |  | 
Method: Least Squares |  |  |  |  | 
Sample: 1993 2014 |  |  |  |  | 
Included observations: 22 |  |  |  |  | 
Variable | Coefficient | Std. Error | t-Statistic | Prob. | Elasticity at 2014 (weather at means)
C | 16948.22 | 3105.043 | 5.458289 | 0.0001 | 
REAL_ELECTRICITY_PRICE(-2) | -1286.671 | 282.2488 | -4.558639 | 0.0003 | -0.2024
REAL_NATURAL_GAS_PRICE(-2) | 188.075 | 60.33242 | 3.117313 | 0.0066 | 0.0297
REAL_INCOME | 0.000214 | 0.0000106 | 20.1258 | 0.0000 | 0.6498
CDD | 2.933447 | 0.694937 | 4.221169 | 0.0006 | 0.0664
HDD | 0.664417 | 0.212405 | 3.128059 | 0.0065 | 0.1084
R-squared | 0.994364 | Mean dependent var |  | 40849.62 | 
Adjusted R-squared | 0.992603 | S.D. dependent var |  | 4697.763 | 
S.E. of regression | 404.0402 | Durbin-Watson stat |  | 1.351322 | 
F-statistic | 564.583 |  |  |  | 
Prob(F-statistic) | 0.000000 |  |  |  | 

## Slide 32: Kentucky
As we did last year, we developed a model using a load adjustment for the closure of the Paducah Gaseous Diffusion Plant (PGDP) in mid-2013
  A large (3 GW) load on the TVA system that accounted for more than 10% of the state’s retail sales

## Slide 33: Kentucky
Change: starting year has been changed from 1994 to 1993
Dependent Variable: ELECTRICITY_SALES |  |  |  |  | 
Method: Least Squares |  |  |  |  | 
Sample: 1993 2014 |  |  |  |  | 
Included observations: 22 |  |  |  |  | 
Variable | Coefficient | Std. Error | t-Statistic | Prob. | Elasticity at 2014 (weather at means)
C | -84835.11 | 10649.88 | -7.965827 | 0.0000 | 
@MOVAV(REAL_ELECTRICITY_PRICE,3) | -2366.73 | 733.9402 | -3.224691 | 0.0053 | -0.1903
@MOVAV(REAL_NATURAL_GAS_PRICE,3) | 770.7436 | 217.1742 | 3.548964 | 0.0027 | 0.0585
POPULATION | 0.037409 | 0.002667 | 14.02876 | 0.0000 | 1.8110
CDD | 4.149048 | 1.885999 | 2.199921 | 0.0429 | 0.0651
HDD | 3.643589 | 1.189408 | 3.063362 | 0.0074 | 0.1929
R-squared | 0.969814 | Mean dependent var |  | 84063.79 | 
Adjusted R-squared | 0.96038 | S.D. dependent var |  | 7646.604 | 
S.E. of regression | 1522.033 | Durbin-Watson stat |  | 2.022556 | 
F-statistic | 102.8079 |  |  |  | 
Prob(F-statistic) | 0.000000 |  |  |  | 

## Slide 34: Louisiana
Due to the historically high rate of customer-owned generation in Louisiana, the relationship between GSP and electricity sales is weak
We were unable to find a model that used GSP as a driver this year
The primary driver in the model (income) has a low elasticity, which means we may end up with an unreasonably low forecast

## Slide 35: Louisiana
As was suggested by one stakeholder group, we will likely construct a second model based on the combination of sales and CHP
  Note: this data is publicly available through EIA
  We will provide the details of this model to the stakeholders and explain the basis for our choice of approaches going forward

## Slide 36: Louisiana
Change: GSP has been replaced by total income
Dependent Variable: ELECTRICITY_SALES |  |  |  |  | 
Method: Least Squares |  |  |  |  | 
Sample: 1990 2014 |  |  |  |  | 
Included observations: 25 |  |  |  |  | 
Variable | Coefficient | Std. Error | t-Statistic | Prob. | Elasticity at 2014 (weather at means)
C | 74640.57 | 7268.002 | 10.26975 | 0.0000 | 
@MOVAV(REAL_ELECTRICITY_PRICE,3) | -4215.296 | 434.2424 | -9.707242 | 0.0000 | -0.3385
REAL_INCOME | 0.000115 | 0.0000123 | 9.370875 | 0.0000 | 0.2503
CDD | 4.621522 | 1.465265 | 3.154052 | 0.0050 | 0.1747
HDD | 4.264524 | 1.328142 | 3.210895 | 0.0044 | 0.0839
R-squared | 0.971777 | Mean dependent var |  | 77122.65 | 
Adjusted R-squared | 0.966132 | S.D. dependent var |  | 6902.32 | 
S.E. of regression | 1270.255 | Durbin-Watson stat |  | 1.802795 | 
F-statistic | 172.1575 |  |  |  | 
Prob(F-statistic) | 0.000000 |  |  |  | 

## Slide 37: Michigan
No changes in drivers or starting year from 2015 model
Dependent Variable: ELECTRICITY_SALES |  |  |  |  | 
Method: Least Squares |  |  |  |  | 
Sample: 1990 2014 |  |  |  |  | 
Included observations: 25 |  |  |  |  | 
Variable | Coefficient | Std. Error | t-Statistic | Prob. | Elasticity at 2014 (weather at means)
C | 54669.24 | 8050.363 | 6.790904 | 0.0000 | 
REAL_ELECTRICITY_PRICE(-2) | -2470.396 | 398.1817 | -6.204191 | 0.0000 | -0.2394
REAL_INCOME/POPULATION | 924.9092 | 155.9355 | 5.931356 | 0.0000 | 0.3565
REAL_GSP | 0.0618 | 0.01773 | 3.485615 | 0.0025 | 0.2477
CDD | 5.475645 | 1.350775 | 4.053705 | 0.0007 | 0.0440
HDD | 1.230438 | 0.557135 | 2.208508 | 0.0397 | 0.0761
R-squared | 0.986593 | Mean dependent var |  | 100050.7 | 
Adjusted R-squared | 0.983065 | S.D. dependent var |  | 8318.694 | 
S.E. of regression | 1082.554 | Durbin-Watson stat |  | 1.946352 | 
F-statistic | 279.6341 |  |  |  | 
Prob(F-statistic) | 0.000000 |  |  |  | 

## Slide 38: Minnesota
Changes: starting year has been changed from 1992 to 1991; electricity price now uses 5-year moving averages instead of 4-year moving averages
Dependent Variable: ELECTRICITY_SALES |  |  |  |  | 
Method: Least Squares |  |  |  |  | 
Sample: 1991 2014 |  |  |  |  | 
Included observations: 24 |  |  |  |  | 
Variable | Coefficient | Std. Error | t-Statistic | Prob. | Elasticity at 2014 (weather at means)
C | 20842.71 | 3265.525 | 6.382653 | 0.0000 | 
@MOVAV(REAL_ELECTRICITY_PRICE,5) | -785.6936 | 286.9386 | -2.738194 | 0.0135 | -0.0981
@MOVAV(REAL_NATURAL_GAS_PRICE,4) | 465.4847 | 120.0009 | 3.87901 | 0.0011 | 0.0503
REAL_INCOME | 0.000154 | 0.00000556 | 27.74229 | 0.0000 | 0.5647
CDD | 6.109774 | 1.119473 | 5.457725 | 0.0000 | 0.0650
HDD | 1.012256 | 0.279173 | 3.625913 | 0.0019 | 0.1328
R-squared | 0.992912 | Mean dependent var |  | 60825.52 | 
Adjusted R-squared | 0.990943 | S.D. dependent var |  | 7158.567 | 
S.E. of regression | 681.2834 | Durbin-Watson stat |  | 1.444467 | 
F-statistic | 504.2722 |  |  |  | 
Prob(F-statistic) | 0.000000 |  |  |  | 

## Slide 39: Mississippi
Change: electricity price now uses 3-year moving averages instead of 2-year moving averages
Dependent Variable: ELECTRICITY_SALES |  |  |  |  | 
Method: Least Squares |  |  |  |  | 
Sample: 1993 2014 |  |  |  |  | 
Included observations: 22 |  |  |  |  | 
Variable | Coefficient | Std. Error | t-Statistic | Prob. | Elasticity at 2014 (weather at means)
C | 13364.2 | 4658.947 | 2.868501 | 0.0111 | 
@MOVAV(REAL_ELECTRICITY_PRICE,3) | -1736.159 | 243.0253 | -7.143943 | 0.0000 | -0.3049
REAL_INCOME(-1) | 0.000136 | 5.15E-05 | 2.643591 | 0.0177 | 0.3000
REAL_GSP | 0.256937 | 0.090669 | 2.833794 | 0.0120 | 0.4921
CDD | 3.047907 | 0.687354 | 4.434262 | 0.0004 | 0.1529
HDD | 1.709259 | 0.615461 | 2.777203 | 0.0135 | 0.0952
R-squared | 0.98633 | Mean dependent var |  | 44657.31 | 
Adjusted R-squared | 0.982059 | S.D. dependent var |  | 4336.682 | 
S.E. of regression | 580.879 | Durbin-Watson stat |  | 2.072365 | 
F-statistic | 230.8954 |  |  |  | 
Prob(F-statistic) | 0.000000 |  |  |  | 

## Slide 40: Missouri
Dependent Variable: ELECTRICITY_SALES |  |  |  |  | 
Method: Least Squares |  |  |  |  | 
Sample: 1998 2014 |  |  |  |  | 
Included observations: 17 |  |  |  |  | 
Variable | Coefficient | Std. Error | t-Statistic | Prob. | Elasticity at 2014 (weather at means)
C | -105234.8 | 11590.11 | -9.079702 | 0.0000 | 
@MOVAV(REAL_ELECTRICITY_PRICE,5) | -2284.499 | 426.4347 | -5.357206 | 0.0002 | -0.2249
POPULATION | 0.017045 | 0.00162 | 10.5187 | 0.0000 | 1.2327
NON_MANUFACTURING_EMP | 0.0321 | 0.005897 | 5.443887 | 0.0002 | 0.9482
CDD | 8.24986 | 0.93112 | 8.860149 | 0.0000 | 0.1597
HDD | 2.472161 | 0.53897 | 4.586823 | 0.0008 | 0.1446
R-squared | 0.990307 | Mean dependent var |  | 78825.52 | 
Adjusted R-squared | 0.985901 | S.D. dependent var |  | 5881.856 | 
S.E. of regression | 698.4027 | Durbin-Watson stat |  | 1.904002 | 
F-statistic | 224.7692 |  |  |  | 
Prob(F-statistic) | 0.000000 |  |  |  | 
No changes in drivers or starting year from 2015 model

## Slide 41: Montana
No changes in drivers or starting year from 2015 model
Dependent Variable: ELECTRICITY_SALES |  |  |  |  | 
Method: Least Squares |  |  |  |  | 
Sample: 1996 2014 |  |  |  |  | 
Included observations: 19 |  |  |  |  | 
Variable | Coefficient | Std. Error | t-Statistic | Prob. | Elasticity at 2014 (weather at means)
C | -524.7233 | 3615.793 | -0.14512 | 0.8870 | 
REAL_ELECTRICITY_PRICE | -1857.406 | 230.4096 | -8.061322 | 0.0000 | -1.0301
@MOVAV(REAL_NATURAL_GAS_PRICE,5) | 497.9886 | 76.74329 | 6.489018 | 0.0000 | 0.2770
REAL_INCOME/POPULATION | 299.0434 | 45.60662 | 6.557017 | 0.0000 | 0.8229
MANUFACTURING_EMP | 0.288485 | 0.072824 | 3.961422 | 0.0019 | 0.3873
CDD | 2.261957 | 0.774918 | 2.918963 | 0.0129 | 0.0768
HDD | 0.962943 | 0.241059 | 3.994629 | 0.0018 | 0.5059
R-squared | 0.938059 | Mean dependent var |  | 13677.86 | 
Adjusted R-squared | 0.907089 | S.D. dependent var |  | 1008.073 | 
S.E. of regression | 307.2734 | Durbin-Watson stat |  | 2.010131 | 
F-statistic | 30.28902 |  |  |  | 
Prob(F-statistic) | 0.000001 |  |  |  | 

## Slide 42: North Dakota
Changes: starting year changes from 1995 to 1994; electricity price now uses 3-year moving averages instead of 2-year moving averages
Dependent Variable: ELECTRICITY_SALES |  |  |  |  | 
Method: Least Squares |  |  |  |  | 
Sample: 1994 2014 |  |  |  |  | 
Included observations: 21 |  |  |  |  | 
Variable | Coefficient | Std. Error | t-Statistic | Prob. | Elasticity at 2014 (weather at means)
C | -9908.14 | 2012.282 | -4.923834 | 0.0002 | 
@MOVAV(REAL_ELECTRICITY_PRICE,3) | -373.9147 | 179.1613 | -2.087029 | 0.0532 | -0.1467
@MOVAV(REAL_NATURAL_GAS_PRICE,3) | 164.4758 | 62.95955 | 2.612404 | 0.0189 | 0.0530
NON_MANUFACTURING_EMP | 0.059875 | 0.00196 | 30.5538 | 0.0000 | 1.4298
HDD | 0.335733 | 0.123958 | 2.708439 | 0.0155 | 0.2612
R-squared | 0.988901 | Mean dependent var |  | 11173.9 | 
Adjusted R-squared | 0.986126 | S.D. dependent var |  | 2824.58 | 
S.E. of regression | 332.6993 | Durbin-Watson stat |  | 1.5623 | 
F-statistic | 356.3902 |  |  |  | 
Prob(F-statistic) | 0.000000 |  |  |  | 

## Slide 43: South Dakota
No changes in drivers or starting year from 2015 model
Dependent Variable: ELECTRICITY_SALES |  |  |  |  | 
Method: Least Squares |  |  |  |  | 
Sample: 1995 2014 |  |  |  |  | 
Included observations: 20 |  |  |  |  | 
Variable | Coefficient | Std. Error | t-Statistic | Prob. | Elasticity at 2014 (weather at means)
C | -19621.55 | 1128.682 | -17.38448 | 0.0000 | 
REAL_ELECTRICITY_PRICE(-2) | -461.3775 | 77.83107 | -5.927934 | 0.0000 | -0.3033
REAL_NATURAL_GAS_PRICE(-2) | 56.99736 | 21.45578 | 2.656504 | 0.0188 | 0.0310
POPULATION | 0.039219 | 0.000887 | 44.19976 | 0.0000 | 2.7102
CDD | 0.484225 | 0.155823 | 3.10753 | 0.0077 | 0.0358
HDD | 0.19127 | 0.0551 | 3.471316 | 0.0037 | 0.1460
R-squared | 0.997687 | Mean dependent var |  | 9729.92 | 
Adjusted R-squared | 0.996861 | S.D. dependent var |  | 1658.558 | 
S.E. of regression | 92.91854 | Durbin-Watson stat |  | 1.833796 | 
F-statistic | 1207.911 |  |  |  | 
Prob(F-statistic) | 0.000000 |  |  |  | 

## Slide 44: Texas
No changes in drivers or starting year from 2015 model
Dependent Variable: ELECTRICITY_SALES |  |  |  |  | 
Method: Least Squares |  |  |  |  | 
Sample: 1996 2014 |  |  |  |  | 
Included observations: 19 |  |  |  |  | 
Variable | Coefficient | Std. Error | t-Statistic | Prob. | Elasticity at 2014 (weather at means)
C | 86745.8 | 17633.71 | 4.919318 | 0.0003 | 
REAL_ELECTRICITY_PRICE(-2) | -3684.416 | 1674.161 | -2.200754 | 0.0464 | -0.0757
REAL_NATURAL_GAS_PRICE(-2) | 2497.617 | 894.5251 | 2.792115 | 0.0153 | 0.0333
REAL_GSP | 0.146033 | 0.005283 | 27.64047 | 0.0000 | 0.5461
CDD | 25.49181 | 4.828415 | 5.27954 | 0.0001 | 0.2328
HDD | 16.33358 | 4.96877 | 3.287248 | 0.0059 | 0.0906
R-squared | 0.989578 | Mean dependent var |  | 334434 | 
Adjusted R-squared | 0.98557 | S.D. dependent var |  | 30848.37 | 
S.E. of regression | 3705.698 | Durbin-Watson stat |  | 2.04072 | 
F-statistic | 246.875 |  |  |  | 
Prob(F-statistic) | 0.000000 |  |  |  | 

## Slide 45: Wisconsin
No changes in drivers or starting year from 2015 model
Dependent Variable: ELECTRICITY_SALES |  |  |  |  | 
Method: Least Squares |  |  |  |  | 
Sample: 1990 2014 |  |  |  |  | 
Included observations: 25 |  |  |  |  | 
Variable | Coefficient | Std. Error | t-Statistic | Prob. | Elasticity at 2014 (weather at means)
C | 20597.33 | 2190.601 | 9.402594 | 0.0000 | 
@MOVAV(REAL_ELECTRICITY_PRICE,3) | -1299.039 | 114.4711 | -11.34818 | 0.0000 | -0.1789
REAL_NATURAL_GAS_PRICE | 257.5846 | 71.14299 | 3.62066 | 0.0018 | 0.0308
REAL_GSP | 0.200844 | 0.003783 | 53.09825 | 0.0000 | 0.7673
CDD | 3.974989 | 0.738156 | 5.385027 | 0.0000 | 0.0376
HDD | 0.569158 | 0.251927 | 2.259222 | 0.0358 | 0.0637
R-squared | 0.99579 | Mean dependent var |  | 63495.47 | 
Adjusted R-squared | 0.994682 | S.D. dependent var |  | 6946.586 | 
S.E. of regression | 506.5929 | Durbin-Watson stat |  | 1.494082 | 
F-statistic | 898.7386 |  |  |  | 
Prob(F-statistic) | 0.000000 |  |  |  | 

## Slide 46: Next Steps
Re-calculate the allocation models to convert state-level forecasts to LRZ level forecasts
Re-calibrate LRZ energy to peak demand conversion models
Incorporate econometric model drivers
Run and validate state econometric models
July workshop

## Slide 47: More Next Steps
Re-calibrate confidence intervals that capture uncertainty of macroeconomic variables
Determine LRZ level energy and peak demand forecasts
Determine MISO system energy and peak demand forecasts
September workshop
Develop forecast report