## Slide 1: The New RO: A Game Changer for Water and Energy
David M. Warsinger
Assistant Prof
Previously:
PostDoc
PostDoc
Ph.D., PostDoc
B.S., M.Eng.
Notes: What are the most critical grand challenges humanity is facing today?
What are the best scientific tools and questions to address these challenges?

## Slide 2
Chart: 
| Capital cost | Energy | Consumables | Labor | Membrane Replacement | Maintenance | Other
 | 0.41 | 0.34 | 0.05 | 0.05 | 0.03 | 0.05 | 0.07
Outline
Lab Intro
Salinity crisis
Context: desalination energy efficiency
Batch fundamentals
New designs
Energy efficiency results
Cost savings
Other technologies

## Slide 3
Research Summary
Briefly describe research areas
Can use one or two illustrations
THERMODYNAMICS & TIME VARYING PROCESSES
Eg. Batch Reverse Osmosis
THERMAL DESALINATION
Eg. Membrane distillation
MEMBRANE NANOMATERIALS
Eg. Photonic membranes
Relevant Scientific Principles
Warsinger Lab Research
Warsinger Water Lab Research

## Slide 4: Salinization Crisis
Saline waters:
reduce crop yields by up to half
carries health and taste concerns for consumption
risks destroying plumbing
Salinization in the Border Region
In Texas, 15% of wells are at risk to high salinity
Surface waters increase substantially in salinity. E.g. Rio Grande increased 5 to 200ppm.
Chaudhuri, S., & Ale, S. (2014). Long-term (1930–2010) trends in groundwater levels in Texas: influences of soils, landcover and water use. Science of the Total Environment, 490, 379-390.
Hot spots of groundwater salinity found in major aquifers across Texas. Shown in black, shallow aquifer measurements exceeded secondary EPA limits in >60% of cases
Notes: Trinity aquifer exceeded limits in 72% of cases

## Slide 5: Salinity Sources
Cyclic salts and
Weathering
Saline
Groundwaters
Geothermal
waters
Waste water
Riparian
Transpiration
Agricultural
Evapotranspiration
Open Water
Evaporation
Consumptive use
Source: Fred Phillips et. al, Salinity Dynamics of the Rio Grande: Shallow Groundwater, Deep Groundwater, and the Rio Grande
Hydrocarbon Exploration
Notes: Ale said groundwater mixing via cross-formational flow between aquifers, seepage from saline plumes and playas, evaporative enrichment, hydrocarbon exploration activities and irrigation return flows led to groundwater salinization in West Texas.

## Slide 6: Desalination Energy Efficiency
2nd law efficiency of leading desalination technologies (Mistr, 2011.)
Other technologies
SWRO
SWRO energy over time
(Adapted from: M. Elimelech, W. A Phillip, Science 333, 712, 2011.)
1
minimum possible
SWRO = Seawater Reverse Osmosis
MSF= Multistage Flash
MED = Multi-Effect Distillation
TVC = Thermal Vapor Compression
Low Carbon Desalination: Status and Research, Development, and Demonstration Needs, J. H. Lienhard, G.P. Thiel, D.M. Warsinger, L. D. Banchik, Massachusetts Institute of Technology

## Slide 7
D. M. Warsinger1, E. W. Tow1, K. Nayar, and J. H. Lienhard V, “Energy efficiency of batch and semi-batch (CCRO) reverse osmosis desalination,” Water Research, vol. 106, pp. 272-282, 2016.
D. M. Warsinger, E. W. Tow, R. McGovern, G. Thiel, and J. H. Lienhard V. Batch Pressure-Driven Membrane Separation with Closed-Flow Loop and Reservoir. Full Patent Application, US non-provisional application No. 15/350,064 November 2016
7
7
Batch Savings
Work in
Friction
Overcoming Membrane Permeability
Instantaneous recovery ratio
Pressure (bar)
Fraction Desalinated
Friction
Overcoming Membrane Permeability
Least Work
Osmotic pressure
Batch Reverse Osmosis
Pure Water
RO
Batch
Osmotic pressure
Terminal Overpressure
Viscous losses each pass
Pump efficiency
Recovery Ratio

## Slide 8
Feed
Pump
Pure Water
RO module
Continuous Reverse Osmosis
D. M. Warsinger1, E. W. Tow1, K. Nayar, and J. H. Lienhard V, “Energy efficiency of batch and semi-batch (CCRO) reverse osmosis desalination,” Water Research, vol. 106, pp. 272-282, 2016.
D. M. Warsinger, E. W. Tow, R. McGovern, G. Thiel, and J. H. Lienhard V. Batch Pressure-Driven Membrane Separation with Closed-Flow Loop and Reservoir. Full Patent Application, US non-provisional application No. 15/350,064 November 2016
Brine

## Slide 9
Feed, single fill
Brine
Recirculation
Variable volume high pressure tank
Brine reject after each cycle
Pump
Pure Water
RO module
Batch RO: High Pressure Tank Concept
Circulation Pump
D. M. Warsinger1, E. W. Tow1, K. Nayar, and J. H. Lienhard V, “Energy efficiency of batch and semi-batch (CCRO) reverse osmosis desalination,” Water Research, vol. 106, pp. 272-282, 2016.
D. M. Warsinger, E. W. Tow, R. McGovern, G. Thiel, and J. H. Lienhard V. Batch Pressure-Driven Membrane Separation with Closed-Flow Loop and Reservoir. Full Patent Application, US non-provisional application No. 15/350,064 November 2016

## Slide 10: 2nd Law Efficiency
Continuous RO
Batch RO
Recovery ratio
Initial salinity [g/kg]
0 10 20 30 40
.9
.8
.7
.6
.5
.4
Recovery ratio
Initial salinity [g/kg]
0 10 20 30 40
.9
.8
.7
.6
.5
.4
60%
40%
20%
0%
Continuous RO
Batch RO
Recovery ratio
Recovery ratio
Initial salinity [g/kg]
0 10 20 30 40
60%
40%
20%
0%
.8
.6
.4
.7
.9
.5
.8
.6
.4
.7
.9
.5
0 10 20 30 40
Initial salinity [g/kg]
Seawater
Groundwater
& Water Reuse

## Slide 11
Chart: Cost category
| U-BRO | BRO | RO | MED | U-BRO | BRO | RO | MED | U-BRO | BRO | RO | MED
Thermal | 0.24303 | 0.28932 | 0.40987 | 0.64393
Electric | 0.24303 | 0.28932 | 0.40987 | 0.082662
Other OpEx | 0.40987 | 0.2417 | 0.28389 | 0.68599
Memb. Replcmt | 0.3074 | 0.13923 | 0.14466 | 0
Operation and maintenance | 0.097645 | 0.10849 | 0.12055 | 0.10394
Other CapEx | 0.40782 | 0.32006 | 0.33609 | 0.34018
Materials & parts | 0.40782 | 0.32006 | 0.33609 | 0.16463
Membranes, pressure vessels | 0.30402 | 0.21626 | 0.2323
Pumps, PX, high alloy steel | 0.18058 | 0.1854 | 0.1977
Civil engineering | 0.088965 | 0.088965 | 0.088965
Energy OpEx CapEx
Relative costs of different components in variants of RO and also MED. Calculated for a system size of 4,000 m3/day.
Includes batch RO (BRO), standard single stage RO (RO), and Multi-effect distillation (MED
Cost savings from Batch + Ultrapermeable Membranes
D. M. Warsinger et. al “IDA 2017 World Congress on Water Reuse and Desalination, São Paulo, Brazil, October 15-20, 2017.

## Slide 12: Applications
Household disinfection for India etc. 70% water savings
Agricultural water use: more efficient, cheaper, water savings
Large-scale desalination
Mining Water treatment
Notes: Ag image: http://waterforfood.nebraska.edu/wp-content/uploads/2015/11/Wheat_Irrigation_Sultanpur-675x381.jpeg
RO unit: http://www.freedrinkingwater.com/images-new/Setuppics/reverse-osmosis-countertop-HL.jpg
Frack water: http://www.powermag.com/Assets/Image/GAS%20POWER%20Direct/GP_050112/050112+F1+Fracking+fig+3.jpg

## Slide 14: Acknowledgements
MIT Team (Lienhard)
Coauthors
John Lienhard
Emily Tow
Jaichander Swaminathan
Grace Connors
Laith Maswadeh
Sandra Cordoba
Bob Boulware
Warsinger Lab (My Lab)

## Slide 15: Questions?

## Slide 16: Water overuse
More than 80% of Rio Grande’s discharge to gulf is diverted for consumption, parts of it run dry (e.g. near Presidio)
Reliance on ground water (“fossil water”) for public needs for TX (36%), AZ (43%), NM (87%)
Dominant consumptive use is agriculture, but industrial use, potable use, cooling towers play a role
Droughts past 14 years:
Border states have high levels
of droughts.
Castillo, et al. to be submitted to Nature Energy (2019)
Notes: I deleted this, wasn’t as relevant I thought:
USA withdraws about 45% of our water for cooling of power plants in production of electricity (Castillo, et al. Scientific American, 2018)

## Slide 17: Batch RO anti-fouling
Warsinger, et. al, “Water Research, vol. pp. 137 384-3942018

## Slide 18: Batch RO Antifouling
Max recovery is increased by short residence times
Warsinger, et. al, “Water Research, vol. pp. 137 384-3942018

## Slide 19: What is Batch?
A set volume of liquid is concentrated
Pressure varies over time
Standard RO
Pressure [bar]
Batch RO
Time [min]
10
20
5
20
Maximum Salinity [g/kg]
3
10
1st cycle
2nd cycle

## Slide 20
Chart: Membrane Permeability [LMH/bar]
| 0.2 | 0.5 | 1 | 2 | 5 | 10 | 20
S=5 g/kg, RR=66% | 2.1875 | 1.1498 | 0.803 | 0.62987 | 0.52612 | 0.49162 | 0.47487
s=35 g/kg, RR=50% | 3.3259 | 2.2877 | 1.944 | 1.7692 | 1.666 | 1.6318 | 1.6014
Ultrapermeable Nanomaterials + Batch: Highest Potential Desalination Efficiencies
Graphene Oxide (GO) Flakes Fabricated by modified Hummers Method.
Past collab w/ Carlo Amadei and Chad Vecitis)
GO
Energy consumption in batch reverse osmosis based on permeability at high (seawater) and low (brackish) salinity.
For ultrapermeable membranes, also considering aquaporin, and improved polyamide TFC fabrication (w/ roll-to-roll methods)
D. M. Warsinger et. al “IDA 2017 World Congress on Water Reuse and Desalination, São Paulo, Brazil, October 15-20, 2017.

## Slide 21: Analysis details
Volume discretization of membrane module for batch models.
The module is divided into unequal volumes, and in each step, equal amounts of permeate are removed from each section and the remaining liquid moves to the next section.
Salinity proﬁles in the membrane module as recovery increases during each cycle for the batch process with 3 ppt at 75% recovery.
Dimensionless distance (The abscissa) is deﬁned as the fraction of the module recovery achieved as the ﬂuid traverses the module (equivalently, i/n). Lines are equally spaced by permeate production; arrows indicate the direction of cycle progression.
Which is discretized across the membrane module for spatial effects, and also calculated over time

## Slide 22: Enhanced Heat Transfer for Thermal Desalination
Enhanced Air-Gap Membrane Distillation Desalination
25 µm
top
50 µm
jumping droplets
nanostructured surface
25 µm
side
Silane-coated copper-oxide-leaf superhydrophobic condensing surfaces
Jumping droplets
Saline feed
Feed preheating
Liquid repelling membrane
Nanoengineered condensing surface
Chart: Pure Water Flux [L/m2hr]
| 22.44 | 15.99 | 12.47 | 10.23 | 8.6820000000000004 | 7.5439999999999996 | 6.6710000000000003 | 5.98 | 5.42 | 4.9550000000000001 | 4.5640000000000001 | 4.2300000000000004 | 3.9420000000000002 | 3.69 | 3.4689999999999999 | 3.2719999999999998 | 3.097 | 2.9390000000000001 | 2.7970000000000002 | 2.6680000000000001 | 2.5499999999999998 | 2.4409999999999998 | 2.3420000000000001 | 2.2509999999999999 | 2.1659999999999999
2.5x | 0.5828 | 1.092 | 1.571 | 2.028 | 2.465 | 2.886 | 3.291 | 3.683 | 4.062 | 4.428 | 4.783 | 5.126 | 5.459 | 5.782 | 6.095 | 6.398 | 6.692 | 6.978 | 7.254 | 7.523 | 7.784 | 8.037 | 8.282 | 8.521 | 8.752
1.8x | 0.5104 | 0.9577 | 1.379 | 1.782 | 2.168 | 2.541 | 2.902 | 3.251 | 3.59 | 3.919 | 4.238 | 4.548 | 4.85 | 5.144 | 5.429 | 5.707 | 5.978 | 6.241 | 6.498 | 6.747 | 6.991 | 7.227 | 7.458 | 7.683 | 7.902
1x | 0.3809 | 0.7158 | 1.033 | 1.336 | 1.629 | 1.913 | 2.189 | 2.458 | 2.721 | 2.977 | 3.227 | 3.471 | 3.711 | 3.945 | 4.174 | 4.399 | 4.619 | 4.834 | 5.045 | 5.252 | 5.454 | 5.653 | 5.848 | 6.039 | 6.226
Mass transfer enhancement
Warsinger et al, J. of Memb.Sci., 2018

## Slide 23: Salinity Gradient Energy Storage
BRO’s higher efficiency makes its energy needs vary more by salinity
Uniquely compatible with demand-response renewable energy
Electric use
or
Figure 1. A new means of grid-scale storage, using reservoirs of high salinity. By integration with desalination, it needs no additional parts, as the desalination membranes provide for PRO (Pressure Retarded Osmosis) electric generation, and desalination already has the pumped hydro components (high pressure pump, pressure recovery turbine)
Seawater or
Water Reuse
Mid
Salinity Reservoir
Pure Water
High Salinity Reservoir
2 modes
1) Desalination (BRO)
1b) Fill when cheap electricity
1a) Fill when normal electricity prices
2) Reverse to generate electricity when prices are high
Electric generation,
stabilization
Grid
Pump
Turbine
Dual-use membranes
2) Electric gen. (PRO)