## Slide 1: Independent Load Forecast Workshop
July 25, 2016

## Slide 2: Stakeholder Comments

## Slide 3: Stakeholder Comments
Documents regarding multicollinearity, heteroscedasticity, first difference models, and comparison of 2015 and 2016 models are provided separately
Inclusion of 2015 data on the load forecast comparison results and results of Louisiana sales+CHP modeling are included in this presentation

## Slide 4: Stakeholder Comments
We were asked a question regarding incorporating a significant change in load if LSEs provide feedback explaining the change
We can make a load adjustment to the forecast based on such changes. This should be done with care to avoid double counting (if the macroeconomic forecast already reflects it) and to ensure the allocation factors assign the load change to the proper LRZ in the state

## Slide 5: Forecast Comparison 2016-2025 2015 ILF vs. Module E vs. 2015 Actual

## Slide 6: Loads Comparison
Comparison charts have been made to show 2015 actual zonal peak/annual loads and projections from ILF
The historical data source (data 1) we used for the 2014 and 2015 ILF studies were discontinued
We have been provided with historical data from a different source (data 4)
Discrepancies between data 1 and 4 exist and may or may not be significant.

## Slide 7: Historical Hourly Loads
Data 1
Metered load with EE/DR/DG adjustment;
Does not include voluntary LMR data.
Used for 2014 and 2015 ILF peak analysis;
Historical hourly loads for LRZ 8,9 and 10 (prior to LRZ formation) were derived;
Contains 2010 to 2014 historical hourly data.
Data 4
SERVM Historical Hourly Load;
Contains voluntary LMR data starting May 2014;
Contains 2010 to 2015 historical hourly load data;
The recorded hourly and annual loads do not exact match data 1’s records;
Peak demand may not occur at the same time as in data 1.

## Slide 8: Summer Peak Discrepancies Between Data Sources (2014)
LRZ | Peak Demand (1) | Peak Demand (4) | Difference | Load Factor (1) | Load Factor (4) | 2014(1) PT | 2014(4) PT
1 | 17,018 | 16,937 | -0.5% | 67% | 66% | 7/21/2014 15:00 | 7/21/2014 14:00
2 | 11,730 | 11,720 | -0.1% | 63% | 63% | 7/22/2014 16:00 | 7/22/2014 16:00
3 | 8,283 | 8,244 | -0.5% | 65% | 65% | 9/4/2014 16:00 | 9/4/2014 16:00
4 | 9,563 | 9,588 | 0.3% | 60% | 60% | 8/25/2014 15:00 | 8/25/2014 15:00
5 | 8,487 | 8,507 | 0.2% | 58% | 58% | 8/25/2014 16:00 | 8/25/2014 16:00
6 | 17,170 | 17,204 | 0.2% | 68% | 66% | 9/5/2014 15:00 | 9/5/2014 14:00
7 | 19,293 | 19,246 | -0.2% | 59% | 59% | 9/5/2014 15:00 | 9/5/2014 15:00
8 | 7,058 | 7,172 | 1.6% | 60% | 59% | 8/25/2014 13:00 | 8/26/2014 15:00
9 | 19,173 | 19,220 | 0.2% | 66% | 66% | 8/22/2014 16:00 | 8/22/2014 16:00
10 | 4,297 | 4,277 | -0.5% | 58% | 57% | 8/6/2014 16:00 | 8/20/2014 16:00
MISO | 114,709 | 114,285 | -0.4% | 67% | 67% | 7/22/2014 16:00 | 7/22/2014 16:00
Red indicates shift in time of peak demand

## Slide 9: Forecast Comparisons
ILF Peak
Allocates state-level forecasts to LRZ levels;
Uses zonal non-coincident factors and coincidence factors to estimate zonal peak loads and system-wide peak load;
Net load: with EE/DR/DG adjustment;
Gross load: without EE/DR/DG adjustment.
MISO Module E Peak
Aggregates asset owner level loads to LRZ levels;
Applies intra-zonal/MISO-wide coincidence factors to convert asset owner level peak loads to zonal peaks and system-wide peak load;
Does not include DR/DG adjustment, may include EE adjustment.

## Slide 10: Comparison Charts
Module E – solid black line
ILF Gross – dashed black line
  ILF Gross high/low bands – hashed area
ILF Net – dashed red line
  ILF Net high/low bands – solid area
2014 actual value from data 1 – blue diamond; 2014 and 2015 actual loads from data 4 – red square;
Metered loads, transmission losses excluded
Historical data based on actual weather conditions; forecasts assume normal weather

## Slide 11: SUFG Peak Gross & Net Forecast vs. Module E vs. 2015 Actual—LRZ 1

## Slide 12: SUFG Peak Gross & Net Forecast vs. Module E vs. 2015 Actual—LRZ 2

## Slide 13: SUFG Peak Gross & Net Forecast vs. Module E vs. 2015 Actual—LRZ 3

## Slide 14: SUFG Peak Gross & Net Forecast vs. Module E vs. 2015 Actual—LRZ 4

## Slide 15: SUFG Peak Gross & Net Forecast vs. Module E vs. 2015 Actual—LRZ 5

## Slide 16: SUFG Peak Gross & Net Forecast vs. Module E vs. 2015 Actual—LRZ 6

## Slide 17: SUFG Peak Gross & Net Forecast vs. Module E vs. 2015 Actual—LRZ 7

## Slide 18: SUFG Peak Gross & Net Forecast vs. Module E vs. 2015 Actual—LRZ 8

## Slide 19: SUFG Peak Gross & Net Forecast vs. Module E vs. 2015 Actual—LRZ 9

## Slide 20: SUFG Peak Gross & Net Forecast vs. Module E vs. 2015 Actual—LRZ 10

## Slide 21: SUFG Peak Gross & Net Forecast vs. Module E vs. 2015 Actual—MISO

## Slide 22: Module E Data PY2016-2017
Module E forecasts provide a series of projections of seasonal loads at the asset owner level (24 months followed by 8 years of summer and winter loads);
Winter loads covers December, January, February, March, April and May;
Summer loads cover June, July, August, September, October and November;
Transmission loss is included;
January to May 2016 monthly loads were from PY2015-2016.

## Slide 23: Forecast Comparisons
ILF
Allocates state-level retail sales forecasts to LRZ levels
Adjust zonal retail sales to metered level sales by adding zonal distribution loss
Net load: with EE/DR/DG adjustment
Gross load: without EE/DR/DG adjustment
Forecast loads by calendar year
MISO Module E
Aggregates asset owner level loads to LRZ levels
Are on a planning year basis that does not correspond to calendar year
Are at the asset level (includes transmission losses)
Does not include DR/DG adjustment, may include EE adjustment

## Slide 24: Module E Data Adjustments
Winter forecasts cover two calendar years (December-May)
  We assumed 5/6 of the winter load was in the 1st calendar year and 1/6 was in the 2nd
Forecast was reduced by the transmission loss percentage to represent metered load level (as in ILF)
  Loss percentage is for peak demand, not annual energy
  This likely overstates losses, resulting in too large of a reduction

## Slide 25: Annual Load Discrepancies Between Data 4 and Data 1
 | 2010 | 2011 | 2012 | 2013 | 2014
1 | 4.88% | -1.02% | -0.90% | -0.89% | -1.01%
2 | -0.40% | -0.42% | -0.42% | -0.91% | -0.73%
3 | -0.63% | -0.81% | -0.88% | -0.65% | -0.66%
4 | -0.32% | -0.18% | -0.45% | -0.43% | -0.34%
5 | -0.18% | -0.21% | -0.11% | 0.05% | 0.17%
6 | 3.76% | -6.14% | -3.15% | -3.12% | -2.37%
7 | -1.92% | -1.06% | -1.71% | -1.82% | -1.10%
8 | -6.73% | -6.26% | -6.51% | -9.68% | -1.04%
9 | -1.42% | -1.08% | -2.34% | -2.86% | -0.44%
10 | -1.30% | -1.78% | -1.73% | -18.12% | -2.25%
MISO | 0.13% | -1.93% | -1.79% | -2.62% | -1.00%
Negative values indicate that Data 4 are smaller than Data 1

## Slide 26: Notes on Data Differences
We have not had an opportunity to determine source of the discrepancies
The 2014 and 2015 ILFs were calibrated to Data 1; calibration to Data 4 would lead to generally lower projections with similar trajectories

## Slide 27: Comparison Charts
Module E – solid black line
ILF Gross – dashed black line
  ILF Gross high/low bands – hashed area
ILF Net – dashed red line
  ILF Net high/low bands – solid area
2014 actual value from data 1 – blue diamond; 2014 and 2015 actual loads from data 4 – red square;
Metered loads, transmission losses excluded
Historical data based on actual weather conditions; forecasts assume normal weather

## Slide 28: SUFG Annual Gross & Net Forecast vs. Module E vs. 2015 Actual—LRZ 1

## Slide 29: SUFG Annual Gross & Net Forecast vs. Module E vs. 2015 Actual—LRZ 2

## Slide 30: SUFG Annual Gross & Net Forecast vs. Module E vs. 2015 Actual—LRZ 3

## Slide 31: SUFG Annual Gross & Net Forecast vs. Module E vs. 2015 Actual—LRZ 4

## Slide 32: SUFG Annual Gross & Net Forecast vs. Module E vs. 2015 Actual—LRZ 5

## Slide 33: SUFG Annual Gross & Net Forecast vs. Module E vs. 2015 Actual—LRZ 6

## Slide 34: SUFG Annual Gross & Net Forecast vs. Module E vs. 2015 Actual—LRZ 7

## Slide 35: SUFG Annual Gross & Net Forecast vs. Module E vs. 2015 Actual—LRZ 8

## Slide 36: SUFG Annual Gross & Net Forecast vs. Module E vs. 2015 Actual—LRZ 9

## Slide 37: SUFG Annual Gross & Net Forecast vs. Module E vs. 2015 Actual—LRZ 10

## Slide 38: SUFG Annual Gross & Net Forecast vs. Module E vs. 2015 Actual—MISO

## Slide 39: Draft State-level Forecasts

## Slide 40: State Forecasts
The state forecasts shown here are gross forecasts in that they do not include an adjustment for EE/DR/DG
2015 and 2016 forecasts are provided to show how different/similar they are

## Slide 41: Arkansas Retail Sales (GWh)
2015 Forecast 2016-2025 projected CAGR - 1.00%
2016 Forecast 2017-2026 projected CAGR - 1.07%
1990-2014 actual CAGR -2.29%
CAGR – Compound Annual Growth Rate
Chart: Arkansas
| 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026
History | 27365.296 | 28440.257 | 28451.112 | 31662.933 | 32619.098 | 34671.434 | 36136.576 | 36857.53 | 39315.195 | 39788.746 | 41611.188 | 41732.449 | 42449.558 | 43108.259 | 43672.36 | 46164.923 | 46635.624 | 47054.891 | 46134.681 | 43173.104 | 48194.285 | 47927.829 | 46859.567 | 46683.034 | 47080.301
2016 Forecast | 47080.301 | 48484.3303 | 49929.3943 | 51305.1037 | 52341.2444 | 52978.8017 | 53358.2707 | 53682.2633 | 54104.1805 | 54641.8679 | 55229.7657 | 55837.491 | 56471.9267
2015 Forecast | 46683.034 | 48372.7445 | 49016.0288 | 49434.2675 | 49916.9739 | 50468.001 | 51279.9109 | 51931.9501 | 52330.3917 | 52697.049 | 53101.4444 | 53592.0171 | 54057.6947

## Slide 42: Illinois Retail Sales (GWh)
2015 Forecast 2016-2025 projected CAGR - 0.63%
2016 Forecast 2017-2026 projected CAGR - 0.64%
1990-2014 actual CAGR - 1.00%
CAGR – Compound Annual Growth Rate
Chart: Illinois
| 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026
History | 111576.776 | 116868.558 | 112520.519 | 117786.375 | 121490.048 | 126231.065 | 125990.381 | 126953.318 | 131697.093 | 132681.539 | 134696.962 | 136033.549 | 138447.313 | 136247.891 | 139253.956 | 144986.215 | 142447.811 | 146055.151 | 144619.914 | 136688.466 | 144760.674 | 142885.567 | 143540.004 | 141804.888 | 141540.287
2016 Forecast | 141540.287 | 143288.9009 | 144913.8956 | 146253.0642 | 147223.6216 | 148543.2266 | 149763.0613 | 150563.7882 | 151306.8075 | 152075.5667 | 153020.6089 | 153894.2255 | 154878.2851
2015 Forecast | 141804.888 | 144437.1911 | 145438.7778 | 146668.8368 | 147576.7594 | 148438.9356 | 149697.9486 | 150907.5184 | 151831.786 | 152653.0025 | 153373.8647 | 154233.9618 | 155133.4796

## Slide 43: Indiana Retail Sales (GWh)
2015 Forecast 2016-2025 projected CAGR – 1.29%
2016 Forecast 2017-2026 projected CAGR – 1.41%
1990-2014 actual CAGR - 1.55%
CAGR – Compound Annual Growth Rate
Chart: Indiana
| 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026
History | 73982.219 | 77033.736 | 76976.815 | 81931.49 | 83807.543 | 87005.957 | 88901.372 | 89146.614 | 92058.825 | 96735.464 | 97774.925 | 97733.968 | 101428.55 | 100467.779 | 103094.263 | 106548.91 | 105664.484 | 109420.15 | 106980.704 | 99311.813 | 105994.376 | 105818.139 | 105173.425 | 105487.389 | 106942.504
2016 Forecast | 106942.504 | 105880.3767 | 107370.9977 | 109633.9242 | 111804.8292 | 113516.0274 | 115102.9799 | 116599.7459 | 118085.6666 | 119640.1259 | 121220.422 | 122735.2429 | 124355.8933
2015 Forecast | 105487.389 | 107383.806 | 108542.3437 | 110042.2531 | 111480.211 | 113013.9193 | 114733.3922 | 116452.7349 | 117928.3 | 119215.0244 | 120594.361 | 122023.0258 | 123492.0855

## Slide 44: Iowa Retail Sales (GWh)
2015 Forecast 2016-2025 projected CAGR – 1.60%
2016 Forecast 2017-2026 projected CAGR – 1.70%
1990-2014 actual CAGR - 1.99%
CAGR – Compound Annual Growth Rate
Chart: Iowa
| 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026
History | 29437.379 | 30781.462 | 30208.072 | 32103.91 | 33039.251 | 34300.919 | 34999.416 | 36147.983 | 37318.292 | 38033.812 | 39087.867 | 39443.755 | 40897.543 | 41207.284 | 40902.773 | 42756.808 | 43336.835 | 45269.523 | 45488.07 | 43641.195 | 45445.269 | 45654.877 | 45709.1 | 46705.216 | 47201.853
2016 Forecast | 47201.853 | 45912.4769 | 47563.2574 | 48178.9466 | 48954.1543 | 49902.3766 | 50834.389 | 51638.6431 | 52454.8364 | 53317.2289 | 54207.1106 | 55131.5245 | 56092.6725
2015 Forecast | 46705.216 | 45934.3581 | 47024.8301 | 47674.9312 | 48339.955 | 49228.4892 | 50054.2446 | 50895.2506 | 51688.6153 | 52532.2146 | 53349.3752 | 54167.1981 | 54982.9243

## Slide 45: Kentucky Retail Sales (GWh)
2015 Forecast 2016-2025 projected CAGR – 1.09%
2016 Forecast 2017-2026 projected CAGR – 1.20%
1990-2014 actual CAGR – 1.07%
CAGR – Compound Annual Growth Rate
Chart: Kentucky
| 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026
History | 61096.874 | 64193.802 | 67067.82 | 68149.184 | 72485.367 | 74548.198 | 77018.734 | 76835.514 | 75850.311 | 79098.015 | 78316.156 | 79975.499 | 87266.835 | 85219.631 | 86521.156 | 89351.466 | 88743.435 | 92404.1 | 93428.414 | 88896.757 | 93569.426 | 89538.341 | 89048.49 | 84763.842 | 78838.924
2016 Forecast | 78838.924 | 77408.1837 | 78232.6597 | 78827.0292 | 79469.2157 | 80683.3311 | 81903.5405 | 83132.4953 | 84172.9176 | 85060.7432 | 85943.1381 | 86881.496 | 87752.3204
2015 Forecast | 84763.842 | 79942.2374 | 79026.0107 | 79893.4824 | 80558.4409 | 81382.6949 | 82430.601 | 83571.7902 | 84641.9681 | 85590.5461 | 86445.5341 | 87272.8052 | 88089.4586

## Slide 46: Louisiana Retail Sales (GWh)
LA will be discussed later

## Slide 47: Michigan Retail Sales (GWh)
2015 Forecast 2016-2025 projected CAGR – 0.88%
2016 Forecast 2017-2026 projected CAGR – 0.98%
1990-2014 actual CAGR – 0.95%
CAGR – Compound Annual Growth Rate
Chart: Michigan
| 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026
History | 82366.869 | 84518.543 | 83840.225 | 87588.602 | 91159.987 | 94701.134 | 96301.566 | 97390.66 | 100506.195 | 103981.006 | 104772.216 | 102409.347 | 104713.52 | 108877.193 | 106606.04 | 110444.563 | 108017.697 | 109296.749 | 105781.271 | 98121.014 | 103649.219 | 105053.558 | 104818.191 | 103038.305 | 103314.098
2016 Forecast | 103314.098 | 105312.5716 | 107564.5606 | 109053.0802 | 111145.3397 | 112750.9282 | 113731.838 | 114225.4378 | 115008.6602 | 115814.2058 | 116976.408 | 118061.6028 | 119066.341
2015 Forecast | 103038.305 | 104734.6124 | 106424.9164 | 107310.7164 | 108651.1608 | 109254.1099 | 110076.7189 | 111628.8941 | 112667.0913 | 113126.7329 | 114011.7228 | 115053.1952 | 116164.8889

## Slide 48: Minnesota Retail Sales (GWh)
2015 Forecast 2016-2025 projected CAGR – 1.67%
2016 Forecast 2017-2026 projected CAGR – 1.68%
1990-2014 actual CAGR – 1.58%
CAGR – Compound Annual Growth Rate
Chart: Minnesota
| 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026
History | 47166.915 | 48754.597 | 47412.154 | 49210.67 | 51155.105 | 53958.771 | 54941.699 | 55674.293 | 56744.047 | 57399.085 | 59782.089 | 60686.852 | 62162.361 | 63087.339 | 63340.315 | 66019.053 | 66769.931 | 68231.182 | 68794.138 | 64004.463 | 67799.706 | 68532.708 | 67988.535 | 68644.103 | 68719.367
2016 Forecast | 68719.367 | 68784.6322 | 70530.2444 | 71822.0126 | 73032.1079 | 74386.1033 | 75775.1301 | 77115.3657 | 78424.6489 | 79653.8243 | 80844.7417 | 82156.6256 | 83472.1244
2015 Forecast | 68644.103 | 68181.2391 | 68835.2784 | 70021.5514 | 71357.4252 | 72436.34 | 73571.856 | 74878.1585 | 76217.0379 | 77553.2845 | 78804.448 | 80022.3847 | 81286.2751

## Slide 49: Mississippi Retail Sales (GWh)
2015 Forecast 2016-2025 projected CAGR – 1.76%
2016 Forecast 2017-2026 projected CAGR – 1.63%
1990-2014 actual CAGR – 1.81%
CAGR – Compound Annual Growth Rate
Chart: Mississippi
| 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026
History | 32127.077 | 33019.383 | 33241.19 | 34749.301 | 36626.569 | 37868.48 | 39622.374 | 40088.725 | 42510.238 | 43979.792 | 45336.178 | 44286.865 | 45451.85 | 45543.881 | 46032.538 | 45901.064 | 46936.437 | 48153.181 | 47721.235 | 46049.154 | 49687.166 | 49337.557 | 48387.675 | 48781.99 | 49408.631
2016 Forecast | 49408.631 | 49061.2055 | 50060.6674 | 51201.7663 | 51925.1555 | 52840.2619 | 53771.1248 | 54767.5224 | 55702.4429 | 56556.7119 | 57412.3488 | 58306.5849 | 59221.9054
2015 Forecast | 48781.99 | 49783.6877 | 49828.8467 | 50722.9239 | 51586.9481 | 52727.316 | 53830.4766 | 54843.6356 | 55722.8265 | 56592.39 | 57499.214 | 58415.5814 | 59342.4131

## Slide 50: Missouri Retail Sales (GWh)
2015 Forecast 2016-2025 projected CAGR – 1.18%
2016 Forecast 2017-2026 projected CAGR – 1.25%
1990-2014 actual CAGR – 1.86%
CAGR – Compound Annual Growth Rate
Chart: Missouri
| 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026
History | 53924.637 | 56514.156 | 54410.855 | 58622.069 | 59692.758 | 62258.967 | 64843.243 | 65711.331 | 69009.936 | 69044.97 | 72642.699 | 73213.157 | 75000.629 | 74239.888 | 74054.296 | 80940.494 | 82015.23 | 85532.85 | 84381.676 | 79897.3 | 86085.117 | 84254.841 | 82435.359 | 83406.957 | 83878.397
2016 Forecast | 83878.397 | 83412.0854 | 85047.442 | 86273.4064 | 87506.8477 | 88608.2223 | 89755.6241 | 90780.9821 | 91844.5067 | 93004.3533 | 94236.2804 | 95416.599 | 96520.3485
2015 Forecast | 83406.957 | 84883.3854 | 85449.4352 | 86862.057 | 87872.8388 | 88763.3905 | 89792.7522 | 91071.0437 | 92262.6391 | 93442.1306 | 94558.3677 | 95625.8405 | 96507.8689

## Slide 51: Montana Retail Sales (GWh)
2015 Forecast 2016-2025 projected CAGR – 1.82%
2016 Forecast 2017-2026 projected CAGR – 1.90%
1990-2014 actual CAGR – 0.30%
CAGR – Compound Annual Growth Rate
Chart: Montana
| 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026
History | 13124.583 | 13406.6 | 13096.382 | 12929.227 | 13184.134 | 13418.523 | 13819.556 | 11917.489 | 14144.832 | 13281.599 | 14579.982 | 11446.658 | 12831.388 | 12824.66 | 12956.782 | 13478.838 | 13814.98 | 15531.985 | 15326.4 | 14353.775 | 13771.453 | 13788.081 | 13863.383 | 14045.174 | 14102.392
2016 Forecast | 14102.392 | 14947.27 | 15284.3911 | 15404.7987 | 15580.9271 | 15647.5981 | 16032.9342 | 16526.1456 | 16969.2245 | 17307.3911 | 17650.7015 | 17913.8073 | 18245.9902
2015 Forecast | 14045.174 | 14967.3283 | 15080.743 | 14955.4373 | 15180.2794 | 15692.0017 | 15967.6001 | 16206.6775 | 16448.8136 | 16744.3756 | 17049.6054 | 17349.6937 | 17584.9501

## Slide 52: North Dakota Retail Sales (GWh)
2015 Forecast 2016-2025 projected CAGR – 1.08%
2016 Forecast 2017-2026 projected CAGR – 1.55%
1990-2014 actual CAGR – 4.06%
CAGR – Compound Annual Growth Rate
Chart: North Dakota
| 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026
History | 7013.85 | 7255.201 | 7128.38 | 7431.958 | 7680.764 | 7882.636 | 8314.159 | 8282.435 | 8220.384 | 9112.193 | 9413.409 | 9809.757 | 10219.353 | 10461.108 | 10516.4 | 10839.99 | 11245.238 | 11905.695 | 12416.074 | 12648.58 | 12956.263 | 13737.016 | 14716.956 | 16032.967 | 18239.732
2016 Forecast | 18239.732 | 16986.086 | 16874.9868 | 17113.5656 | 17513.1036 | 17891.5799 | 18262.5263 | 18525.8269 | 18787.6819 | 19055.5677 | 19294.3342 | 19486.8068 | 19648.7851
2015 Forecast | 16032.967 | 17100.4515 | 17637.0947 | 18020.2027 | 18320.5302 | 18612.43 | 18903.0521 | 19195.7109 | 19377.454 | 19524.3312 | 19678.2458 | 19797.5949 | 19849.5586

## Slide 53: South Dakota Retail Sales (GWh)
2015 Forecast 2016-2025 projected CAGR – 2.02%
2016 Forecast 2017-2026 projected CAGR – 2.17%
1990-2014 actual CAGR – 2.82%
CAGR – Compound Annual Growth Rate
Chart: South Dakota
| 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026
History | 6333.893 | 6685.14 | 6493.846 | 6904.707 | 7174.054 | 7413.542 | 7736.162 | 7772.548 | 7824.031 | 7922.354 | 8282.74 | 8626.999 | 8936.801 | 9079.99 | 9213.844 | 9811.017 | 10056.387 | 10603.301 | 10974.086 | 11010.118 | 11356.149 | 11679.6 | 11734.21 | 12209.799 | 12354.726
2016 Forecast | 12354.726 | 12256.4063 | 12742.0459 | 12994.7828 | 13285.5101 | 13640.0687 | 13966.1114 | 14249.6864 | 14549.458 | 14863.8601 | 15181.8513 | 15485.1577 | 15764.771
2015 Forecast | 12209.799 | 12275.4901 | 12550.55 | 12980.3932 | 13286.1962 | 13484.7051 | 13743.665 | 14104.5112 | 14434.4513 | 14740.681 | 15012.0838 | 15283.798 | 15539.4817

## Slide 54: Texas Retail Sales (GWh)
2015 Forecast 2016-2025 projected CAGR – 1.91%
2016 Forecast 2017-2026 projected CAGR – 2.00%
1990-2014 actual CAGR – 2.09%
CAGR – Compound Annual Growth Rate
Chart: Texas
| 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026
History | 237415.127 | 240351.787 | 239431.038 | 250084.413 | 258179.737 | 263278.592 | 278449.583 | 286703.509 | 304704.764 | 301844.18 | 318262.529 | 318044.174 | 320845.849 | 322685.955 | 320614.84 | 334258.262 | 342724.213 | 343828.582 | 347814.647 | 345351.42 | 358457.55 | 376065.116 | 365104.131 | 378817.254 | 389669.82
2016 Forecast | 389669.82 | 398998.1288 | 400467.9101 | 407682.6423 | 417086.4493 | 426911.5533 | 436158.6433 | 444081.3918 | 452832.4593 | 461551.4055 | 470286.8528 | 478539.1012 | 487358.0855
2015 Forecast | 378817.254 | 388016.2726 | 396660.3199 | 406074.9879 | 412071.914 | 418876.3952 | 428672.1837 | 439010.8477 | 448429.6559 | 457270.9305 | 465521.5739 | 473611.4999 | 481278.7529

## Slide 55: Wisconsin Retail Sales (GWh)
2015 Forecast 2016-2025 projected CAGR – 1.49%
2016 Forecast 2017-2026 projected CAGR – 1.53%
1990-2014 actual CAGR – 1.45%
CAGR – Compound Annual Growth Rate
Chart: Wisconsin
| 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026
History | 49198.028 | 51032.208 | 50925.09 | 53156.402 | 55411.611 | 57966.904 | 58743.628 | 60094.002 | 62061.221 | 63547.448 | 65146.487 | 65218.293 | 66999.296 | 67241.494 | 67975.709 | 70335.683 | 69820.749 | 71301.3 | 70121.827 | 66286.439 | 68752.417 | 68611.622 | 68820.09 | 69124.043 | 69494.755
2016 Forecast | 69494.755 | 69762.289 | 71401.2331 | 73182.7126 | 74892.4835 | 76212.9313 | 77266.6155 | 78231.3326 | 79381.3367 | 80577.3875 | 81723.8505 | 82773.5806 | 83919.8137
2015 Forecast | 69124.043 | 69958.6401 | 71126.6025 | 72208.816 | 73346.2626 | 74527.0266 | 75922.1896 | 77218.6109 | 78285.4356 | 79295.324 | 80359.6941 | 81444.152 | 82522.1545

## Slide 56: Louisiana Model
Model presented in the last workshop
- Personal Income used as macro economic variable
Dependent Variable: ELECTRICITY_SALES |  |  |  |  | 
Method: Least Squares |  |  |  |  | 
Sample: 1990 2014 |  |  |  |  | 
Included observations: 25 |  |  |  |  | 
Variable | Coefficient | Std. Error | t-Statistic | Prob. | Elasticity at 2014 (weather at means)
C | 74640.57 | 7268.002 | 10.26975 | 0.0000 | 
@MOVAV(REAL_ELECTRICITY_PRICE,3) | -4215.296 | 434.2424 | -9.707242 | 0.0000 | -0.3385
REAL_INCOME | 0.000115 | 0.0000123 | 9.370875 | 0.0000 | 0.2503
CDD | 4.621522 | 1.465265 | 3.154052 | 0.0050 | 0.1747
HDD | 4.264524 | 1.328142 | 3.210895 | 0.0044 | 0.0839
R-squared | 0.971777 | Mean dependent var |  | 77122.65 | 
Adjusted R-squared | 0.966132 | S.D. dependent var |  | 6902.32 | 
S.E. of regression | 1270.255 | Durbin-Watson stat |  | 1.802795 | 
F-statistic | 172.1575 |  |  |  | 
Prob (F-statistic) | 0.000000 |  |  |  | 

## Slide 57: Louisiana Model
Problems with Previous Model
  Personal Income has a relatively low elasticity (0.25) and a low growth rate (2.05% for the period of 2017-2026).
  The model produces an unreasonably low electricity sales forecast of -0.11% over the period of 2017-2026.
Alternative approaches were tested and will be presented.

## Slide 58: Louisiana Model
Option 1
  Electricity sales as dependent variable
  GSP as macro-economic variable
  2005 data dropped as an outliner (Hurricanes Katrina and Rita)
Dependent Variable: ELECTRICITY_SALES |  |  |  |  | 
Method: Least Squares |  |  |  |  | 
Sample: 1990 2004 2006 2014 |  |  |  |  | 
Included observations: 24 |  |  |  |  | 
Variable | Coefficient | Std. Error | t-Statistic | Prob. | Elasticity at 2014 (weather at means)
C | 43231.93 | 9063.392 | 4.769951 | 0.0001 | 
REAL_ELECTRICITY_PRICE(-2) | -2880.37 | 494.0632 | -5.829963 | 0.0000 | -0.2313
REAL_GSP | 0.182654 | 0.028914 | 6.317075 | 0.0000 | 0.4319
CDD | 4.680232 | 2.400735 | 1.9495 | 0.0662 | 0.1765
HDD | 6.425083 | 1.936429 | 3.318006 | 0.0036 | 0.1269
R-squared | 0.942101 | Mean dependent var |  | 77111.55 | 
Adjusted R-squared | 0.929912 | S.D. dependent var |  | 7050.546 | 
S.E. of regression | 1866.571 | Durbin-Watson stat |  | 1.716599 | 
F-statistic | 77.28978 |  |  |  | 
Prob(F-statistic) | 0.000000 |  |  |  | 

## Slide 59: Louisiana Retail Sales (GWh)
2015 Forecast 2016-2025 projected CAGR – 1.87%
2016 Forecast 2017-2026 projected CAGR – 0.62%
1990-2014 actual CAGR – 1.47%
Chart: Louisiana - Option 1
| 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026
History without CHP | 63825.89 | 64704.299 | 65098.33 | 67755.825 | 70131.806 | 72827.19 | 75269.095 | 75885.666 | 77716.091 | 78266.678 | 80690.346 | 74692.751 | 79260.989 | 77769.322 | 79737.112 | 77389.17 | 77467.748 | 79566.937 | 78725.774 | 78669.582 | 85079.692 | 86369.081 | 84730.743 | 85807.932 | 90628.316
2016 Forecast - Option 1 | 90628.316 | 85815.2554 | 85764.2722 | 88703.0798 | 90569.0327 | 91021.6079 | 91327.1025 | 91252.3628 | 91427.8282 | 91993.7441 | 92795.8647 | 93200.5875 | 93812.4211
2015 Forecast | 85807.932 | 86325.9552 | 87904.7125 | 90520.197 | 92021.2341 | 93833.9273 | 96031.0477 | 98002.6049 | 99732.1845 | 101410.9617 | 103042.4812 | 105061.1318 | 106923.2036

## Slide 60: Louisiana Model
Option 2
  Electricity sales + CHP as dependent variable
  GSP excluding Mining GSP (oil and gas drilling)as macro-economic variable
Dependent Variable: ELECTRICITY_SALES+CHP |  |  |  |  | 
Method: Least Squares |  |  |  |  | 
Sample: 1990 2014 |  |  |  |  | 
Included observations: 25 |  |  |  |  | 
Variable | Coefficient | Std. Error | t-Statistic | Prob. | Elasticity at 2014 (weather at means)
C | 58418.34 | 16094.09 | 3.629801 | 0.0017 | 
REAL_ELECTRICITY_PRICE(-2) | -4559.912 | 857.4264 | -5.318138 | 0.0000 | -0.2716
REAL_GSP_EXCLUDE_MINING | 0.281547 | 0.038688 | 7.277368 | 0.0000 | 0.4617
CDD | 6.894593 | 4.106805 | 1.678822 | 0.1087 | 0.2010
HDD | 7.988799 | 3.567171 | 2.239534 | 0.0366 | 0.1212
R-squared | 0.927427 | Mean dependent var |  | 99988.41 | 
Adjusted R-squared | 0.912912 | S.D. dependent var |  | 11740.93 | 
S.E. of regression | 3464.826 | Durbin-Watson stat |  | 1.435208 | 
F-statistic | 63.8959 |  |  |  | 
Prob(F-statistic) | 0.000000 |  |  |  | 

## Slide 61: Louisiana Retail Sales (GWh)
2015 Retail Sales Forecast 2016-2025 projected CAGR – 1.87%
2016 Retail Sales Forecast 2017-2026 projected CAGR – 0.95%
1990-2014 actual CAGR – 1.47%
Chart: Louisiana - Option 2
| 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026
History without CHP | 63825.89 | 64704.299 | 65098.33 | 67755.825 | 70131.806 | 72827.19 | 75269.095 | 75885.666 | 77716.091 | 78266.678 | 80690.346 | 74692.751 | 79260.989 | 77769.322 | 79737.112 | 77389.17 | 77467.748 | 79566.937 | 78725.774 | 78669.582 | 85079.692 | 86369.081 | 84730.743 | 85807.932 | 90628.316
History with CHP | 79653.89 | 80189.299 | 81475.33 | 84364.825 | 86572.806 | 89265.19 | 91822.095 | 94766.666 | 98329.091 | 100825.678 | 103442.346 | 96650.751 | 100718.989 | 106141.322 | 106262.112 | 99499.17 | 104592.748 | 106471.937 | 104929.774 | 104489.582 | 113420.692 | 114741.081 | 112765.743 | 116133.932 | 122185.316
2016 Forecast - Option 2 | 122185.316 | 115647.6177 | 116107.78 | 121028.4148 | 124023.8622 | 124750.584 | 125307.1836 | 125148.4934 | 125338.006 | 126149.0054 | 127375.6401 | 128039.0282 | 129008.0522
2016 Forecast - Option 2-CHP | 90628.316 | 84090.6177 | 84550.78 | 89471.4148 | 92466.8622 | 93193.584 | 93750.1836 | 93591.4934 | 93781.006 | 94592.0054 | 95818.6401 | 96482.0282 | 97451.0522
2015 Forecast | 85807.932 | 86325.9552 | 87904.7125 | 90520.197 | 92021.2341 | 93833.9273 | 96031.0477 | 98002.6049 | 99732.1845 | 101410.9617 | 103042.4812 | 105061.1318 | 106923.2036

## Slide 62: Pros & Cons
Option 1
  Consistent with approach in other states and preference for public data sources
  Growth may be low considering expected new loads; some indication that all may not show up or be delayed
Option 2
  Relies on arbitrary assumption that CHP will remain constant across forecast horizon
  Relies on non-standard economic driver
  Results in slightly higher forecast

## Slide 63: Other Option
We could incorporate a load adjustment for new large loads that have a high degree of certainty
  We would need information on the size and timing of those loads

## Slide 64: Allocation Factors

## Slide 65: Reminder
Allocation factors are used to assign state forecasts to particular LRZs
Small loads in Oklahoma & Tennessee that are in LRZ 8 are included with Arkansas
Kentucky is combined with Indiana and Montana is combined with North Dakota per MISO request
Illinois and Missouri were also analyzed at the Chicago and St. Louis Metropolitan Statistical Area

## Slide 66: Historical Load Shares (MISO vs. non-MISO)
State | MISO Sales (Megawatthours) | Non-MISO Sales (Megawatthours) | 2010 | 2011 | 2012 | 2013 | 2014 | Average
AR | 34,008,348 | 13,071,953 | 70.57% | 70.39% | 70.52% | 70.45% | 72.23% | 70.83%
IA | 43,920,136 | 3,281,717 | 92.92% | 93.04% | 93.22% | 92.92% | 93.05% | 93.03%
IL | 49,309,489 | 92,230,798 | 34.55% | 34.80% | 33.91% | 34.59% | 34.84% | 34.54%
IN | 85,104,043 | 21,838,461 | 78.92% | 79.00% | 79.22% | 79.22% | 79.58% | 79.19%
KY | 11,400,836 | 67,438,088 | 11.87% | 12.43% | 12.82% | 13.51% | 14.46% | 13.02%
IN+KY | 96,504,879 | 89,276,549 | 47.49% | 48.49% | 48.78% | 49.94% | 51.95% | 49.33%
LA | 83,987,702 | 6,640,614 | 91.77% | 91.74% | 92.06% | 92.20% | 92.67% | 92.09%
MI | 99,263,860 | 4,050,238 | 96.01% | 96.16% | 96.21% | 96.10% | 96.08% | 96.11%
MN | 67,870,999 | 848,368 | 98.73% | 98.73% | 98.84% | 98.75% | 98.77% | 98.76%
MO | 41,332,442 | 42,545,955 | 49.67% | 49.47% | 50.33% | 49.52% | 49.28% | 49.65%
MS | 22,014,990 | 27,393,641 | 45.89% | 45.24% | 44.78% | 44.73% | 44.56% | 45.04%
MT | 803,729 | 13,298,663 | 5.36% | 5.40% | 5.55% | 5.57% | 5.70% | 5.51%
ND | 10,935,451 | 7,304,281 | 71.49% | 70.52% | 66.16% | 65.40% | 59.95% | 66.71%
ND+MT | 11,739,180 | 20,602,944 | 37.35% | 37.90% | 36.76% | 37.46% | 36.30% | 37.15%
SD | 3,120,871 | 9,233,855 | 26.87% | 26.07% | 26.02% | 25.32% | 25.26% | 25.91%
TX | 21,815,593 | 367,854,227 | 5.66% | 5.46% | 5.99% | 5.74% | 5.60% | 5.69%
WI | 69,494,755 | 0 | 100.0% | 100.0% | 100.0% | 100.0% | 100.0% | 100.0%

## Slide 67: Historical Load Shares (LRZ)
MISO LRZ | State | State Level MISO Load Fraction |  |  |  |  | 
 |  | Average | 2010 | 2011 | 2012 | 2013 | 2014
1 | IA | 1.77% | 1.77% | 1.76% | 1.73% | 1.78% | 1.83%
 | IL | 0.0002% | 0.0002% | 0.0002% | 0.0002% | 0.0002% | 0.0002%
 | MI | 0.14% | 0.14% | 0.14% | 0.13% | 0.14% | 0.14%
 | MN | 96.81% | 96.73% | 96.76% | 96.93% | 96.89% | 96.76%
 | ND+MT | 37.15% | 37.35% | 37.90% | 36.76% | 37.46% | 36.30%
 | SD | 24.10% | 24.97% | 24.28% | 24.24% | 23.51% | 23.51%
 | WI | 16.77% | 16.59% | 16.94% | 16.23% | 17.02% | 17.05%
2 | MI | 5.09% | 5.22% | 5.28% | 4.89% | 4.94% | 5.14%
 | WI | 83.23% | 83.41% | 83.06% | 83.77% | 82.98% | 82.95%
3 | IA | 91.25% | 91.14% | 91.28% | 91.48% | 91.15% | 91.22%
 | IL | 1.42% | 1.42% | 1.45% | 1.42% | 1.42% | 1.40%
 | MN | 1.95% | 2.00% | 1.97% | 1.91% | 1.86% | 2.01%
 | SD | 1.81% | 1.90% | 1.79% | 1.77% | 1.80% | 1.75%
4 | IL | 33.11% | 33.12% | 33.35% | 32.49% | 33.17% | 33.44%
5 | MO | 49.41% | 49.41% | 49.22% | 50.09% | 49.28% | 49.06%
6 | IN+KY | 49.29% | 47.49% | 48.49% | 48.60% | 49.94% | 51.95%
7 | MI | 90.88% | 90.65% | 90.75% | 91.19% | 91.02% | 90.80%
8 | AR | 70.83% | 70.57% | 70.39% | 70.52% | 70.45% | 72.23%
 | MO | 0.24% | 0.26% | 0.25% | 0.24% | 0.23% | 0.22%
 | TX | 0.01% | 0.01% | 0.01% | 0.01% | 0.01% | 0.01%
9 | LA | 92.09% | 91.77% | 91.74% | 92.06% | 92.20% | 92.67%
 | TX | 5.68% | 5.65% | 5.46% | 5.98% | 5.73% | 5.59%
10 | MS | 45.04% | 45.89% | 45.24% | 44.78% | 44.73% | 44.56%

## Slide 68: 2016 Allocation Factors
With the exception of IN+KY and MT+ND, all allocation factors were determined from the average of the 2010 – 2014 load shares
Chicago MSA has a similar growth as Illinois for GSP, so no adjustment
St. Louis MSA has lower population but higher non-manufacturing employment, which tend to cancel each other out, so no adjustment

## Slide 69: IN+KY
The closure of the Paducah Gaseous Diffusion Plant in non-MISO Kentucky (mid-year 2013) caused a shift in the LRZ 6 load share for IN+KY
We use the 2014 load share, since it is the first year where the plant is shut down for the entire year

## Slide 70: MT+ND
Growth and contraction in the Bakken region, which results in a spike in statewide consumption in 2014, occurs primarily outside the MISO region
This volatility should not be reflected in the LRZ 1 forecast
We use the average of 2010 – 2013 load factors to determine the allocation factor

## Slide 71
MISO Allocation Factors - AR
Chart: 
| 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026
LRZ8 | 0.7057 | 0.7039 | 0.7052 | 0.7045 | 0.7223 | 0.70832 | 0.70832 | 0.70832 | 0.70832 | 0.70832 | 0.70832 | 0.70832 | 0.70832 | 0.70832 | 0.70832 | 0.70832 | 0.70832
non-MISO | 0.2943 | 0.2961 | 0.2948 | 0.2955 | 0.2777 | 0.29168 | 0.29168 | 0.29168 | 0.29168 | 0.29168 | 0.29168 | 0.29168 | 0.29168 | 0.29168 | 0.29168 | 0.29168 | 0.29168

## Slide 72
MISO Allocation Factors - IA
Chart: 
| 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026
LRZ 1 | 0.0177 | 0.0176 | 0.0173 | 0.0178 | 0.0183 | 0.01774 | 0.01774 | 0.01774 | 0.01774 | 0.01774 | 0.01774 | 0.01774 | 0.01774 | 0.01774 | 0.01774 | 0.01774 | 0.01774
LRZ 3 | 0.9114 | 0.9128 | 0.9148 | 0.9115 | 0.9122 | 0.91254 | 0.91254 | 0.91254 | 0.91254 | 0.91254 | 0.91254 | 0.91254 | 0.91254 | 0.91254 | 0.91254 | 0.91254 | 0.91254
non-MISO | 0.0709 | 0.0696 | 0.0679 | 0.0707 | 0.0695 | 0.06972 | 0.06972 | 0.06972 | 0.06972 | 0.06972 | 0.06972 | 0.06972 | 0.06972 | 0.06972 | 0.06972 | 0.06972 | 0.06972

## Slide 73
MISO Allocation Factors - IL
Chart: 
| 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026
LRZ 1 | 2e-06 | 2e-06 | 2e-06 | 2e-06 | 2e-06 | 2e-06 | 2e-06 | 2e-06 | 2e-06 | 2e-06 | 2e-06 | 2e-06 | 2e-06 | 2e-06 | 2e-06 | 2e-06 | 2e-06
LRZ 3 | 0.0142 | 0.0145 | 0.0142 | 0.0142 | 0.014 | 0.01422 | 0.01422 | 0.01422 | 0.01422 | 0.01422 | 0.01422 | 0.01422 | 0.01422 | 0.01422 | 0.01422 | 0.01422 | 0.01422
LRZ 4 | 0.3312 | 0.3335 | 0.3249 | 0.3317 | 0.3344 | 0.33114 | 0.33114 | 0.33114 | 0.33114 | 0.33114 | 0.33114 | 0.33114 | 0.33114 | 0.33114 | 0.33114 | 0.33114 | 0.33114
non-MISO | 0.6546 | 0.652 | 0.6609 | 0.6541 | 0.6516 | 0.65464 | 0.65464 | 0.65464 | 0.65464 | 0.65464 | 0.65464 | 0.65464 | 0.65464 | 0.65464 | 0.65464 | 0.65464 | 0.65464

## Slide 74
MISO Allocation Factors – IN+KY
Chart: 
| 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026
LRZ 6 | 0.4749 | 0.4849 | 0.486 | 0.4994 | 0.5195 | 0.5195 | 0.5195 | 0.5195 | 0.5195 | 0.5195 | 0.5195 | 0.5195 | 0.5195 | 0.5195 | 0.5195 | 0.5195 | 0.5195
non-MISO | 0.5251 | 0.5151 | 0.514 | 0.5006 | 0.4805 | 0.4805 | 0.4805 | 0.4805 | 0.4805 | 0.4805 | 0.4805 | 0.4805 | 0.4805 | 0.4805 | 0.4805 | 0.4805 | 0.4805

## Slide 75
MISO Allocation Factors – LA
Chart: 
| 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026
LRZ 9 | 0.9177 | 0.9174 | 0.9206 | 0.922 | 0.9267 | 0.92088 | 0.92088 | 0.92088 | 0.92088 | 0.92088 | 0.92088 | 0.92088 | 0.92088 | 0.92088 | 0.92088 | 0.92088 | 0.92088
non-MISO | 0.0823 | 0.0826 | 0.0794 | 0.078 | 0.0733 | 0.07912 | 0.07912 | 0.07912 | 0.07912 | 0.07912 | 0.07912 | 0.07912 | 0.07912 | 0.07912 | 0.07912 | 0.07912 | 0.07912

## Slide 76
MISO Allocation Factors – MI
Chart: 
| 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026
LRZ 1 | 0.0014 | 0.0014 | 0.0013 | 0.0014 | 0.0014 | 0.00138 | 0.00138 | 0.00138 | 0.00138 | 0.00138 | 0.00138 | 0.00138 | 0.00138 | 0.00138 | 0.00138 | 0.00138 | 0.00138
LRZ 2 | 0.0522 | 0.0528 | 0.0489 | 0.0494 | 0.0514 | 0.05094 | 0.05094 | 0.05094 | 0.05094 | 0.05094 | 0.05094 | 0.05094 | 0.05094 | 0.05094 | 0.05094 | 0.05094 | 0.05094
LRZ 7 | 0.9065 | 0.9075 | 0.9119 | 0.9102 | 0.908 | 0.90882 | 0.90882 | 0.90882 | 0.90882 | 0.90882 | 0.90882 | 0.90882 | 0.90882 | 0.90882 | 0.90882 | 0.90882 | 0.90882
non-MISO | 0.0399 | 0.0383 | 0.0379 | 0.039 | 0.0392 | 0.03886 | 0.03886 | 0.03886 | 0.03886 | 0.03886 | 0.03886 | 0.03886 | 0.03886 | 0.03886 | 0.03886 | 0.03886 | 0.03886

## Slide 77
MISO Allocation Factors – MN
Chart: 
| 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026
LRZ 1 | 0.9673 | 0.9676 | 0.9693 | 0.9689 | 0.9676 | 0.96814 | 0.96814 | 0.96814 | 0.96814 | 0.96814 | 0.96814 | 0.96814 | 0.96814 | 0.96814 | 0.96814 | 0.96814 | 0.96814
LRZ 3 | 0.02 | 0.0197 | 0.0191 | 0.0186 | 0.0201 | 0.0195 | 0.0195 | 0.0195 | 0.0195 | 0.0195 | 0.0195 | 0.0195 | 0.0195 | 0.0195 | 0.0195 | 0.0195 | 0.0195
non-MISO | 0.0127 | 0.0127 | 0.0116 | 0.0125 | 0.0123 | 0.01236 | 0.01236 | 0.01236 | 0.01236 | 0.01236 | 0.01236 | 0.01236 | 0.01236 | 0.01236 | 0.01236 | 0.01236 | 0.01236

## Slide 78
MISO Allocation Factors – MO
Chart: 
| 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026
LRZ 5 | 0.4941 | 0.4922 | 0.5009 | 0.4928 | 0.4906 | 0.49412 | 0.49412 | 0.49412 | 0.49412 | 0.49412 | 0.49412 | 0.49412 | 0.49412 | 0.49412 | 0.49412 | 0.49412 | 0.49412
LRZ 8 | 0.0026 | 0.0025 | 0.0024 | 0.0023 | 0.0022 | 0.0024 | 0.0024 | 0.0024 | 0.0024 | 0.0024 | 0.0024 | 0.0024 | 0.0024 | 0.0024 | 0.0024 | 0.0024 | 0.0024
non-MISO | 0.5033 | 0.5053 | 0.4967 | 0.5049 | 0.5072 | 0.50348 | 0.50348 | 0.50348 | 0.50348 | 0.50348 | 0.50348 | 0.50348 | 0.50348 | 0.50348 | 0.50348 | 0.50348 | 0.50348

## Slide 79
MISO Allocation Factors – MS
Chart: 
| 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026
LRZ 10 | 0.4589 | 0.4524 | 0.4478 | 0.4473 | 0.4456 | 0.4504 | 0.4504 | 0.4504 | 0.4504 | 0.4504 | 0.4504 | 0.4504 | 0.4504 | 0.4504 | 0.4504 | 0.4504 | 0.4504
non-MISO | 0.5411 | 0.5476 | 0.5522 | 0.5527 | 0.5544 | 0.5496 | 0.5496 | 0.5496 | 0.5496 | 0.5496 | 0.5496 | 0.5496 | 0.5496 | 0.5496 | 0.5496 | 0.5496 | 0.5496

## Slide 80
MISO Allocation Factors – ND+MT
Chart: 
| 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026
LRZ 1 | 0.3735 | 0.379 | 0.3676 | 0.3746 | 0.363 | 0.37367 | 0.37367 | 0.37367 | 0.37367 | 0.37367 | 0.37367 | 0.37367 | 0.37367 | 0.37367 | 0.37367 | 0.37367 | 0.37367
non-MISO | 0.6265 | 0.621 | 0.6324 | 0.6254 | 0.637 | 0.62633 | 0.62633 | 0.62633 | 0.62633 | 0.62633 | 0.62633 | 0.62633 | 0.62633 | 0.62633 | 0.62633 | 0.62633 | 0.62633

## Slide 81
MISO Allocation Factors – SD
Chart: 
| 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026
LRZ 1 | 0.2497 | 0.2428 | 0.2424 | 0.2351 | 0.2351 | 0.24102 | 0.24102 | 0.24102 | 0.24102 | 0.24102 | 0.24102 | 0.24102 | 0.24102 | 0.24102 | 0.24102 | 0.24102 | 0.24102
LRZ 3 | 0.017536 | 0.018048 | 0.017746 | 0.017942 | 0.019009 | 0.018056 | 0.018056 | 0.018056 | 0.018056 | 0.018056 | 0.018056 | 0.018056 | 0.018056 | 0.018056 | 0.018056 | 0.018056 | 0.018056
non-MISO | 0.73276 | 0.73915 | 0.73985 | 0.74696 | 0.74589 | 0.74092 | 0.74092 | 0.74092 | 0.74092 | 0.74092 | 0.74092 | 0.74092 | 0.74092 | 0.74092 | 0.74092 | 0.74092 | 0.74092

## Slide 82
MISO Allocation Factors – TX
Chart: 
| 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026
LRZ 8 | 5.6869e-05 | 5.7769e-05 | 6.0218e-05 | 6.2654e-05 | 6.4688e-05 | 6.044e-05 | 6.044e-05 | 6.044e-05 | 6.044e-05 | 6.044e-05 | 6.044e-05 | 6.044e-05 | 6.044e-05 | 6.044e-05 | 6.044e-05 | 6.044e-05 | 6.044e-05
LRZ 9 | 0.0565 | 0.0546 | 0.0598 | 0.0573 | 0.0559 | 0.05682 | 0.05682 | 0.05682 | 0.05682 | 0.05682 | 0.05682 | 0.05682 | 0.05682 | 0.05682 | 0.05682 | 0.05682 | 0.05682
non-MISO | 0.94344 | 0.94534 | 0.94014 | 0.94264 | 0.94404 | 0.94312 | 0.94312 | 0.94312 | 0.94312 | 0.94312 | 0.94312 | 0.94312 | 0.94312 | 0.94312 | 0.94312 | 0.94312 | 0.94312

## Slide 83
MISO Allocation Factors – WI
Chart: 
| 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026
LRZ 1 | 0.1659 | 0.1694 | 0.1623 | 0.1702 | 0.1705 | 0.16766 | 0.16766 | 0.16766 | 0.16766 | 0.16766 | 0.16766 | 0.16766 | 0.16766 | 0.16766 | 0.16766 | 0.16766 | 0.16766
LRZ 2 | 0.8341 | 0.8306 | 0.8377 | 0.8298 | 0.8295 | 0.83234 | 0.83234 | 0.83234 | 0.83234 | 0.83234 | 0.83234 | 0.83234 | 0.83234 | 0.83234 | 0.83234 | 0.83234 | 0.83234
non-MISO | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0

## Slide 84: Next Steps

## Slide 85: September Workshop
We will present updated energy to peak conversion
We will cover the draft forecast results at LRZ and MISO level
Please send your comments and suggestions for improvements