## Slide 1
Legend:
1. Gray boxes denote task by Applicant.
2. White boxes denote task by Jurisdiction Entity.
3. Dashed line boxes denote forms.
Applicant submits full Drainage/Stormwater Permit Application to the Jurisdiction Entity for review
Drainage/Stormwater Permit Application review by Jurisdiction Entity
Drainage/Stormwater Permit
approved by Jurisdiction Entity
Application complies with Stormwater Ordinance and Technical Standards
Does not comply
Applicant modifies plans and resubmits to Jurisdiction Entity
Form by Jurisdiction Entity:
Documentation of
Non-Compliance Issues
Form by Jurisdiction Entity:
Drainage/Stormwater Permit
Submittal by Applicant:
Application Checklist
Construction Plans
Drainage Technical Report
SWPPP for Construction Site
Post-Construction SWPPP Items
Applicant submits online Notice of Intent to IDEM and notifies Jurisdiction Entity prior to starting construction
Pre-Construction Meeting
held with Jurisdiction Entity
Applicant constructs project
Major construction is completed: Applicant submits as-built plans to Jurisdiction Entity
Site is stabilized: Applicant requests termination verification inspection
from Jurisdiction Entity
Form by Jurisdiction Entity:
Termination Inspection Checklist
(that confirms site compliance)
Form by Jurisdiction Entity:
Termination Inspection
Checklist (that documents non-compliance issues)
Applicant addresses/resolves Termination Inspection Checklist non-compliance issues
Applicant monitors construction activities; complies with terms and conditions of this Ordinance and the Stormwater permit
Site complies with termination requirements
Does not comply
Form by Applicant:
Construction Site Inspection and Maintenance Log
Form by Applicant:
Certificate of Completion
Notifications by Applicant:
On-Line Submittal to IDEM of:
Signed/Approved Termination Inspection Checklist from Jurisdiction Entity
IDEM Notice of Termination
Notifications by Applicant:
On-Line Submittal of Notice of Intent to IDEM
E-mail notification to Jurisdiction Entity