GAS CHROMATOGRAPHY PURDUE UNIVERSITY INSTRUMENT VAN PROJECT DETERMINING THE IDENTITY OF ALCOHOLS IN UNKNOWN

MIXTURES USING THE GAS CHROMATOGRAPH

(Revised: 2-6-96)

INTRODUCTION

You have already seen how gas chromatography is used to determine percent composition of mixtures. We can also use gas chromatography to identify substances in an unknown mixture.

You will use a process called co-injection or spiking to identify alcohols in a n unknown misture. Co-injection involves adding a known substance to the unknown. If this known substance is also present in the unknown, then the peak for that substance will be larger in the spiked sample than in the the unspiked sample. If the known is not a substance present in the unknown, then an extra peak will appear in the spiked sample compared to the unspiked sample. This technique will be used with each of four known alcohols. Results will be obtained by analyzing the peak heights and the time required for peaks to appear on the chromatogram.

If you cannot decide which of the two alcohols corresponds to a peak you will rerun the unknown and two unknown samples spiked with the alcohols in question. The attenuation and chart speed wil be changed to widen and separate the peaks.

PURPOSE

To determine the identity of the substance causing each peak in the chromatogram of an unknown mixture by spiking samples to be analyzed in the gas chromatograph.

SAFETY

GOGGLES MUST BE WORN AT ALL TIMES!

Cautions: 1) Injection port is very hot.

2) Syringe needle is delicate and sharp. Use extreme

caution when handling.

3) Do not adjust knobs and control buttons on the

machines. They have already been set for you!

MATERIALS

Gas Chromatograph

10 μL syringe

Unknown samples A, B, C & D (one per group)

Known samples: n-butyl alcohol (1-butanol)

t-butyl alcohol (2-methyl-2-propanol)

n-propyl alcohol (1-propanol)

isopropyl alcohol (2-propanol)

PROCEDURE

When it is your turn, you will perform several tasks. Read through all procedures before you begin.

1. You will be assigned an unknown mixture (A, B, C or D) to analyze by spiking. Record this letter on your data table.

2. Clean the syringe:

a. Draw 10 μL of your unknown mixture into the syringe and expel it onto a paper

towel.

b. Repeat once more.

3. Gather unknown sample mixture:

a. Insert syringe into your unknown mixture and draw 1 μL into the syringe.

b. Remove the syringe from the bottle, cap the bottle and draw 5 μL of air into the

syringe.

4. Run the sample:

a. Check to be sure baseline needle is set and recorder is turned on and in standby

mode.

b. Carefully insert syringe needle into INJECTION PORT A. Remember: The

port will be very hot. Quickly and smoothly depress the plunger and remove

the syringe.

c. As this is being done, have a partner turn the recorder to run and record the

following information on your chromatogram:

a. Attenuator setting

b. Sample size

c. Identity of sample

d. Chart speed

e. Group name or number

5. Record your observations on the data sheet. While chromatogram is running, have one member of your group prepare a spiked sample of your unknown. (follow steps 6 & 7).

6 Clean the syringe:

a. Draw 10 μL of your unknown mixture into the syringe and expel it onto a paper

towel.

b. Repeat once more.

7. Gather unknown + known mixture:

a. Insert syringe into your unknown mixture and draw 1 μL intothe syringe.

b. Draw 1 μL of air into the same syringe and wipe off the needle with a

Kimwipe©.

c. Insert the needle into n-propyl alcohol and draw 1 μL into the syringe (along

with the other sample).

d. Draw 5 μL of air into syringe and close all bottle caps.

8. Run the sample:

a. Check to be sure the last chromatograph has finished. Do not inject until it has!

b. Carefully insert syringe needle intoINJECTION PORT A. Remember: port

will be very hot. Quickly and smoothly depress the plunger and remove the

syringe.

c. As this is being done, have a partner record the following information on your

chromatogram:

a. Attenuator setting

b. Sample size

c. Identity of sample

d. Chart speed

e. Group name or number

9. Record your information on the data sheet. While this is running, prepare to run a second spiked sample of the unknown mixture. Follow the same instructions as before, this time running your unknown + isopropyl alcohol.

10. Repeat the entire procedure (steps 6-9) twice more using:

unknown + t-butyl alcohol

unknown + n-butyl alcohol

11) Remove the chromatogram after you are finished.

| UNKNOWN | SPIKE 1 n-butyl alcohol | SPIKE 2 t-butyl alcohol | SPIKE 3 n-propyl alcohol | SPIKE 4 isopropyl alcohol |
| --- | --- | --- | --- | --- |
| unknown sample letter |
| amount used |
| number of peaks observed |
| attentuation |
| chart speed |

CONCLUSIONS

At this point, you should have a good idea about the identity of the alcohols in your unknown mixture by camparing chromatograms of the unknown mixture with spiked samples. Identify the alcohols if you are able to do so!

If you are unable to decide which of the two alcohols are responsible for a peak, you will need to analyze three more samples (unknown, 2 unknown samples each spiked with one of the alcohols in question) at different instrument settings. Before running the three samples, please notify your teacher that you will be doing the following:

a. Increase the attenuation from 8 to 16.

b. Increase the chart speed from 2 cm/min to 3 cm/min.

Identify thye alcohols in the unknown mixture that corresponds to each peak in the chromatogram of the unknown mixture.

DATA TABLE #2

GAS CHROMATOGRAPHY PURDUE UNIVERSITY INSTRUMENT VAN PROJECT

| identity of substance | identity of substance | identity of substance |
| --- | --- | --- |
| Peak 1 |
| Peak 2 |
| Peak 3 |