An organic compound’s melting point is one of several physical properties by which it is identified. A physical property is a property that is intrinsic to a compound when it is pure. Since melting points are relatively easy and inexpensive to determine, they are handy identification tools to the organic chemist.

If you want to use the melting point to identify a solid compound which you have isolated in the lab, you will need to compare its melting point with that of the true compound. Melting points are listed in various sources of scientific data, as referenced in physical data tables on the world wide web, or in chemistry handbooks (like the Handbook of Chemistry and Physics).

Melting Point Data Table

| Compound | M.P. | Formula |
| --- | --- | --- |
| stearic acid |  |  |
| citric acid |  |  |
| hydroquinone |  |  |
| benzoic acid |  |  |
| benzoyl peroxide |  |  |
| pyrogallic acid |  |  |
| l-ascorbic acid |  |  |
| salicylic acid |  |  |
| acetylsalicylic acid |  |  |

I.  PURPOSE

The purpose of this experiment is to determine the melting points of various organic compounds and to use these to identify unknowns.

II.  PROCEDURE

A.  Obtain a capillary melting point tube and a known compound.

B.  Loading the melting point capillary.  Place a VERY SMALL quantity of the solid of interest on a watch glass, and use a stirring rod to grind the solid to a powder. Use a spatula to gather the powder into a small pile. Stick the open end of a melting point capillary into the pile to a depth of about 1 mm, then invert the capillary and tap the sealed end on the bench to encourage the solid to drop to the bottom. The height of solid in the capillary should be no more than 1-2 mm. If you have more solid than this in the tube, you should try to shake some out, then reseat the solid at the bottom of the tube.

D.  Place the capillary melting point tube in the DigiMelt apparatus chamber.  Start with a setting so that the temperature rises slowly.  The sample should be observed continuously, so that the melting point of the sample is not missed.  Heat slowly to acquire the most accurate results.  Record the melting range, which begins when the sample first starts to melt and ends when the sample is completely melted.

E.  Obtain two unknown samples and determine their melting ranges.  Identify the unknowns by comparing the data for the melting points that you have obtained in the Melting Point Data Table above.

.

III.  DATA

Known Compounds:

| compound |  | melting range | - oC |
| --- | --- | --- | --- |
| compound |  | melting range | - oC |

First Unknown:

| compound | Unknown # ___________ | melting range | - oC |
| --- | --- | --- | --- |
| identity of compound |  |  |  |

Second Unknown:

| compound | Unknown # ___________ | melting range | - oC |
| --- | --- | --- | --- |
| identity of compound |  |  |  |

IV.  QUESTIONS

1.  Define the "melting point" of a substance.

________________________________________________________________________________________________

2.  What is the purpose of determining melting points?

________________________________________________________________________________________________

3.  What class of compounds did we use for this lab?  ____________________________________  Why?

________________________________________________________________________________________________

4.  Why could the rate of heating influence the melting point?

________________________________________________________________________________________________

Name __________________________    Date __________________

Lab Partner _____________________________

# LAB – Determination of Melting Points

| Compound | M.P. | Formula |
| --- | --- | --- |
| 4. stearic acid | 69-72 |  |
| 3. citric acid | 153 |  |
| 2. hydroquinone | 172 |  |
| 9. benzoic acid | 122.4 |  |
| benzoyl peroxide | 103 - 105 |  |
| 5. pyrogallic acid | 131 |  |
| 6. l-ascorbic acid | 192 |  |
| 7. salicylic acid | 159 |  |
| 8. acetylsalicylic acid | 136 (decomposes) |  |
| Checked all of the above for dangers or hazards, treat them like you would any compound. None were found to be toxic, many are used in daily creams and medications |  |  |

F.  Time permitting, pulverize a mixture of two known substances used for practice with a mortar and pestle, and determine the melting point of the mixture.

(OPTIONAL)  Melting points of mixture _______:  _________(C and  _________(C

Components of mixture _______ are ________________________and 	________________________

# Text boxes

# Chemistry 2

# LAB – Determination of Melting Points