ACID-BASE TITRATION USING A pH METER

(Revised: 1-25-93)

INTRODUCTION

In an acid-base titration, the important information to obtain is the equivalence point.   If there are a given number of moles of acid in the titration flask,  the equivalence point is reached when that same number of moles of base have been added from the buret.  The molarity of the base can then be calculated since the number of moles of base added is the same as the number of moles of acid in the flask, and the volume of the base added is also known.  Similarly, if the number of moles of acid in the titration flask is unknown, it can be calculated for the equivalence point if the molarity of the base and the volume of base added are known.

Often the pH of the solution will change dramatically at the equivalence point.  An acid-base indicator works by changing color over a given pH range.  If an indicator which changes color near the equivalence point is chosen, there is also a dramatic change in the color of the indicator at the equivalence point because the pH changes so rapidly.

In a potentiometric acid-base titration, an indicator is not necessary.  A pH meter is used to measure the pH as base is added in small increments (called aliquots) to an acid solution.  A graph is then made with pH along the vertical axis and volume of base added along the horizontal axis.  From this graph the equivalence point can be determined and the molarity of the base calculated.

OBJECTIVES

1.	To perform a potentiometric titration of an acidic solution of known molarity.

2.	To graph the volume of base added vs the pH and to determine the equivalence point.

3.	To calculate the molarity of the basic solution.

SAFETY

1.	Wear your goggles and apron at all times during this experiment.

2.	The HCl solution is corrosive.  If any is spilled, you should neutralize it with sodium bicarbonate solution.  If you should get some on your skin, neutralize it , and then wash it off with plenty of water.  In either case, notify your teacher immediately.

3.	The NaOH solution is caustic.  If you get any on your skin, flush the affected area with plenty of water.  Notify your teacher immediately.

MATERIALS

pH meter with standard buffers of pH 4.0, pH 7.0, and pH 10.0

50 mL buret

buret clamp and ring stand

magnetic stirrer with small stir bar

250 mL beaker

HCl solution of known molarity

NaOH Solution of unknown molarity

PROCEDURE

1.	Obtain about 100 mL of 0.15 M HCl in a clean, dry beaker.  This beaker should be labeled.  Never pour any solution back into this beaker.  Once the solution has been poured into the buret, it should be discarded into the sink or waste container.

2.	Rinse your buret with distilled water.  Then use a small amount of the 0.l5 M HCl solution to rinse the buret. (Pour about 10 ml of the HCl solution into the buret.  Let some of it flow through the tip.  Pour the rest of the HCl solution out the top of the buret, rotating the buret as you pour.)  The rinsing solution should be discarded into the sink.  Repeat this rinsing procedure twice more. Fill the buret to some point higher than the markings with the HCl solution and then carefully let the HCl solution out into a waste container until the bottom of the meniscus is on the 0.00 line.

3.	Obtain about 100 mL of NaOH solution in another clean, dry beaker.  This beaker should also be labeled.  Never pour any solution back into this beaker.  Once the solution has been poured into the buret, it should be discarded into the sink or waste container.  Rinse and fill the other buret as indicated in step 2.

4.	Standardize the pH meter (Refer to the specific instructions for the pH meter that you will be using)

5.	Place a 250 mL beaker under the buret containing the 0.15 M HCl and let out approximately 20 mL into the beaker.  Record the mL of HCl added to the beaker.

6.	Carefully drop a magnetic stirring bar into the beaker containing the HCl solution.  Set the beaker on the magnetic stirring motor and position the buret containing the NaOH solution and the pH electrode as shown in the diagram. Carefully turn on the stirring motor and make sure that the stirring bar does not hit the electrode.  Adjust the stirring speed as directed by your teacher.

7.	Set up your data table to include mL of NaOH added and the pH of the solution.  You should allow for as many as 50 mL of solution.

8.	Measure and record the pH of the solution before any NaOH has been added.

9.	Add 1.0 mL of NaOH solution carefully from the buret.  Record the pH when it has stabilized.  Add another 1.0 mL of NaOH and record the pH. Continue adding NaOH in 1.0 mL increments until you have obtained a pH reading greater than 12.

10.	Remove the pH electrode from the solution, rinse it with distilled water, and store it as directed by your teacher.

11.	The solutions may be discarded down the sink.  Rinse the burets with distilled water and place it upside down in the buret holder to drain.

CALCULATIONS

1.	Make a graph of the pH vs mL of NaOH added.  The pH should be on the vertical axis and the mL of NaOH should be on the horizontal axis. The graph should be of such a size that 1 mL is represented by 1 square on the graph and the pH scale is spread out as much as possible.

2.	There should be a region on your graph where the slope is very steep.  Determine the midpoint of this region.  This is the equivalence point.  Record the mL of NaOH added at the equivalence point as determined from the graph.

3.	Use the relationship:  MAVA = MBVB to determine the molarity of the base.

LAB WRITTEN BY: PRU PHILLIPS